## Slide 1: Cranes and Derricks
29 CFR 1926 - Subpart CC
Notes: Revised 03/13/2026
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
In this course, we will discuss the following:
  Scope of the standard
  Ground conditions
  Assembly/disassembly
  Power line safety
  Inspections
  Fall protection
  Operator and signal person qualifications
  Signals
  Tower cranes
1926.1400

## Slide 3: Scope
Applies to power-operated equipment, when used in construction, that can hoist, lower and horizontally move a suspended load.
Applies to the same equipment when used with attachments.
1926.1400

## Slide 4: Scope
Specific exclusions
  Machinery while it is converted or adapted for non-hoisting/lifting use
    Such as power shovels, excavators and concrete pumps
Limited exclusions
  Digger derricks, articulating/knuckle-boom truck cranes
1926.1400(c)

## Slide 5: Equipment Not Covered
Digger derricks
  Equipped with auger for drilling holes to set poles
  Handling materials installed or removed from poles
1926.1400(c)(4)

## Slide 6: Equipment Not Covered
Articulating/knuckle-boom truck crane
  Delivering materials to construction site
  Transferring materials from truck crane onto structure using fork/cradle at end of boom
1926.1400(c)(17)(ii)

## Slide 7: Equipment Covered
Articulating/knuckle-boom truck crane
  Holding, supporting or stabilizing material to facilitate construction activity
  Handling prefabricated components
  Handling structural steel members
1926.1400(c)(17)(iii)(A)–(C)

## Slide 8: Equipment Covered
Articulating/knuckle-boom truck crane
1926.1400(c)(17)(iii)(A)–(C)

## Slide 9: Definitions
Competent person – A person who is capable of identifying existing and predictable hazards … and who has authorization to take prompt corrective measures to eliminate them.
Qualified person – A person who, by possession of a recognized degree, certificate, or professional standing, or who by extensive knowledge, training and experience, successfully demonstrated an ability to solve/resolve problems relating to the subject matter, the work, or the project.
1926.1401

## Slide 10: Definitions
Dedicated spotter (power lines) – person who meets requirements of 1926.1428 (signal person qualifications)
  Responsibility to watch separation between power line and equipment
  Ensure communication with operator that minimum approach distance not breached
1926.1401

## Slide 11: Definitions
Controlling entity
  Provide adequate conditions
    Firm, drained, and graded
    So that with the use of supporting materials, the equipment manufacturer’s specifications for adequate support and degree of level of the equipment are met.
1926.1402(c)(1)

## Slide 12: Ground Conditions
1926.1402(c)(1)
Adequate conditions
  Firm?
  Drained?
  Graded?

## Slide 13: Ground Conditions
Inform user of the equipment and operator of the location of hazards beneath the equipment set-up area.
  Voids
  Tanks
  Utilities
1926.1402(c)(2)

## Slide 14: Assembly/Disassembly
Two options
  Manufacturer procedures
  Employer procedures
1926.1403

## Slide 15: Assembly/Disassembly
Crane assembly and disassembly procedures
  Comply with manufacturer or employer procedures
  Supervision – Competent-qualified person = A/D director
    Knowledge of procedures
    Review of procedures
    Ensure crew members understand their tasks and associated hazards
Tower crane
  Pre-erection inspection
    Each crane component inspected by qualified person
1926.1403, .1404, .1435

## Slide 16: Assembly/Disassembly
Site and ground conditions must be adequate
When required, block under outrigger floats
1926.1404(h)

## Slide 17: Assembly/Disassembly
1926.1404(h)

## Slide 18: Power Line Safety
Power lines presumed energized
  Unless utility owner/operator confirms lines deenergized
  Visibly grounded at worksite
1926.1407(f)

## Slide 19: Power Line Safety
Identify the work zone
  Demarcating boundaries (such as with flags, or a device such as a range limit device or range control warning device) or
  Define the work zone as the area 360 degrees around the equipment, up to equipment’s maximum working radius.
1926.1408
WorkSafe BC

## Slide 21
Table A – Minimum Clearance Distances
Voltage (nominal, kV, Minimum clearance
alternating current) distance (feet)
up to 50 10
over 50 to 200 15
over 200 to 350 20
over 350 to 500 25
over 500 to 750 35
over 750 to 1,000 45
over 1,000 (as established by the utility owner/
operator or registered professional
engineer who is a qualified person with respect to electrical power transmission and distribution)
1926.1408
Power Line Safety

## Slide 22: Intentionally Working Closer Than Table A Zone
Power line owner – sets minimum approach distance
Planning meeting – minimum procedures
Must Show:
Staying outside zone is infeasible
All of the following are required:
Limit access to essential workers
Prohibit non-operator workers from touching above insulating link
Properly ground crane
Deactivate automatic re-energizer
Insulating line cover-up installed
Dedicated spotter
Elevated warning line or barricade
Insulating link/device
Nonconductive rigging
Range limiter (if equipped)
Nonconductive tag line (if used)
Barricades - 10 feet from equipment
Infeasible to deenergize & ground

## Slide 23: Power Line Safety
Equipment traveling under power line with no load
  Boom/mast and boom/mast support system lowered sufficiently to meet requirements
  Clearances in Table T maintained
  Effects of speed and terrain on
  equipment movement
  Dedicated spotter
  Precautions for traveling in poor visibility
1926.1411(a) – (b)

## Slide 24: Power Line Safety
Table T – Minimum Clearance Distances While
Traveling With No Load
Voltage (nominal, kV, While traveling – Minimum alternating current) clearance distance (feet)
up to 0.75 4
over .75 to 50 6
over 50 to 345 10
over 345 to 750 16
over 750 to 1,000 20
over 1,000 (as established by the utility owner/operator
or registered professional engineer who is a
qualified person with respect to electrical
power transmission and distribution)
1926.1411

## Slide 25: Electric Utilities
Employers whose employees are qualified to perform power distribution and transmission work
  Deemed compliance with §§1926.1407 through 1926.1411 when performing work covered by Subpart V work in accordance with 1910.269(p)
1926.1400(g)
Adobe Stock Photo

## Slide 26: Inspections
Visual inspection by competent person during each shift
Monthly inspection by competent person – with documentation
1926.1412(d)-(e)

## Slide 27: Inspections
Other inspections required under this section done by qualified person – with documentation
  Annual/comprehensive
  Post-assembly
  Repaired/adjusted equipment
  Modified equipment
  Severe service
  Equipment not in regular use
1926.1412(a)-(c)

## Slide 28: Inspections
Type of Inspection | Who Inspects
Modified or repaired/adjusted | Qualified person
Post-assembly | Qualified person
Shift | Competent person
Monthly | Competent person
Annual | Qualified person
1926.1412(a)-(c)

## Slide 29: Safety Devices
Required and operational at all times:
  Crane level indicator
  Boom stops (except for derricks and hydraulic booms)
  Jib stops (except for derricks)
  Foot pedal brakes with locks
  Hydraulic outrigger jacks/hydraulic stabilizer
  jacks with integral holding device
  Equipment on rails with rail clamps/stops
  Horn
1926.1415(a)-(b)

## Slide 30: Operational Aids
Operations must not begin unless the listed operational aids are in proper working order, except when being repaired and a specified temporary alternative measure is used.
Category 1
  Boom hoist limiting device, luffing jib limiting device, anti two-blocking device
  Must be repaired no later than 7 calendar days after the deficiency occurs.
Category 2
  Boom angle or radius indicator, boom length indicator, load weighing devices, jib angle indicator, outrigger/stabilizer position sensor/monitor, and hoist drum rotation indicator
  Must be repaired no later than 30 calendar days after the deficiency occurs.
1926.1416(b)

## Slide 31: Operations
When manufacturer procedures are unavailable, the employer must develop and ensure compliance with procedures necessary for safe operation of equipment and attachments.
Procedures for the operational controls must be developed by a qualified person.
Procedures, including rated capacities, recommended operating speeds, special hazard warnings, instructions, and operator’s manual, must be available in the cab at all times for use by the operator.
1926.1417(b)-(c)

## Slide 32: Operations
Operator must not engage in any practice or activity that diverts their attention while engaged in operating the equipment, such as the use of cellular phones (other than when used for signal communications).
1926.1417(d)
Adobe Stock Photo

## Slide 33: Fall Protection
Boom walkways
Steps, handholds, ladders, grabrails, guardrails, and railings
1926.1423(c)

## Slide 34: Fall Protection
Personal fall arrest and
positioning device systems
Anchorage criteria
Training
1926.1423(d)-(k)
Adobe Stock Photo

## Slide 35: Fall Protection
1926.1423(d)-(k)

## Slide 36: Keeping Clear of the Load
When employees are hooking, unhooking, or guiding the load, or in the initial connection of a load to a component/structure and are within the fall zone:
  Materials being hoisted must be rigged by a qualified rigger
  Hooks with self-closing latches must be used
Only employees receiving a load are permitted within the fall zone when a load is being landed.
1926.1425(c)-(d)

## Slide 37: Rigging
Rigging work done by qualified rigger
  During assembly/disassembly
  When workers are within the fall zone to handle a load
1926.1404(r)(1) & .1425(c)(3)

## Slide 38: Tower Crane Requirements
Foundations and structural supports
  Designed by manufacturer or professional engineer
Plumb tolerance
  Verified by qualified person
Climbing procedures
Pre- and post-erection inspection
  By qualified person
Post-erection load test
Monthly/annual inspection
1926.1435

## Slide 39: Operator Qualification/Certification
Testing Criteria
Knowledge (written test):
  Controls/performance characteristics
  Calculate capacity
  Preventing power line contact
  Ground conditions & equipment support
  Use and locate info in operating manual
  Appendix C subjects
Practical test
1926.1427
Option 1:
Accredited testing organization
Option 2:
Audited employer program
Option 3:
U.S. military
Option 4:
Government entity
Notes: 1926.1427(b) Option (1): Certification by an accredited crane operator testing organization.
Testing organization accredited by nationally recognized accrediting agency
  National Commission for Certifying Agencies (NCCA)
  American National Standards Institute (ANSI)
Accredited crane/derrick operator testing organizations
  Crane Institute of America (CIA)
    Crane Institute Certification (CIC)
  National Commission for the Certification of Crane Operators (NCCCO)
  North American Crane Bureau (NACB)
    National Commission for
    Construction, Education, &
    Research (NCCER)
Different tests for Different capacity/type of equipment
Determines compliance with testing & test administration criteria
Develops and administers the tests (written & practical) to certify operators
1926.1427(c) Option (2): Qualification by an audited employer program.
Specifies the audit conducted in accordance with nationally recognized auditing standards
Employer-administered written & practical tests
Compliance with testing & test administration criteria
1926.1427(d) Option (3): Qualification by the U.S. military.
Issues Operator Qualification
1926.1427(e) Option (4): Licensing by a government entity.
State/local government authority that oversees licensing office
Determines license office complies with testing/test administration criteria

## Slide 40: Operator Qualification/Certification
Portable |  | Valid
Accredited Testing Organization | YES * | 5 years
Audited Employer Program | NO | 5 years
U.S. Military License | NO * | Set by issuing entity
Government License | NO * Valid only in jurisdiction | Set by issuing entity, not > 5 years
Subject to state and local requirements and whether or not the military/state training meets accredited requirements. |  | 
1926.1427

## Slide 41: Operator Qualification/Certification
Operator qualification or certification not required:
  Equipment with rated hoisting/lifting capacity of 2,000 pounds or less
  Derricks
  Sideboom cranes
Operator trained on safe
operation of equipment
1926.1427(a)

## Slide 42: Operator Qualification/Certification
Employer must provide the qualification or certification at no cost to operators.
1926.1427(a)-(4)

## Slide 43: Language Requirements
Tests under this section may be administered in any language the operator candidate understands.
Operator’s certificate must note the language in which the test was given.
Equipment operation materials must be in the language of certification.
1926.1427(h)

## Slide 44: Signals
Signal person provided
  Load not in view of operator
  View in direction of travel is obstructed
  Due to site specific safety concerns
Types of signals
  Hand
  Voice
  Audible
  New signals
Hand signal chart posted on equipment or at site
1926.1419 and .1422

## Slide 45: Signal Persons Qualifications
Know and understand type of signals used
Competent in using signals
Basic understanding of equipment operation and limitations
Know and understand relevant requirements
Demonstrate knowledge through an oral or written test and practical test
1926.1425(c)

## Slide 46: Signal Persons Qualifications
Option | Documentation | Portable
Option (1): Third party qualified evaluator | Yes | Yes
Option (2): Employer’s qualified evaluator | Yes | No
1926.1428(c)

## Slide 47: Training Requirements
Overhead powerlines
Signal persons
Operators
Competent persons/qualified persons
Crush/pinch points
Tag-out
1926.1430(a)-(f)
Notes: (g).

## Slide 48: Training Administration
Employees trained and evaluated on their understanding of the information provided
Refresher training
Training provided at no cost to employee
1926.1430(g)
Adobe Stock Photo

## Slide 49: Summary
In this course, we discussed the following:
  Scope of the standard
  Ground conditions
  Assembly/disassembly
  Power line safety
  Inspections
  Fall protection
  Tower cranes
  Operator and signal person qualifications
  Training
1926.1400
Notes: Photo inserted by Julie Martin on 3/12/26, used per Adobe stock subscription/license

## Slide 50: Thank You For Attending!
Final Questions?