## Slide 1
Top 10 Most Frequently Citied Serious Violations in FFY 2022
29 CFR 1926 - Construction
Presented by:
Notes: Revised: 10/23
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
In this course, we will discuss the Top Ten most frequently cited serious Construction Industry violations for federal fiscal year (FFY) 2022.
Citations and violations issued from October 1, 2021, thru September 30, 2022, in North Carolina.
NCDOL Photo Library

## Slide 3: Fall Protection
Number 1: Residential Construction
  Each employee engaged in residential construction activities 6 feet (1.8 m) or more above lower levels shall be protected.
    Personal fall arrest system
    Guardrail systems
    Safety net system
1926.501(b)(13)

## Slide 4: Fall Protection
1926.501(b)(13)
Where is fall protection required?
NCDOL Photo Library

## Slide 5: Personal Protective Equipment
Number 2: Eye and Face Protection - General Requirements
  Provide employees with eye and face protection when machines or operations present potential eye or face injury from physical, chemical, or radiation agents.
1926.102(a)(1)

## Slide 6: Eye and Face Protection
Is the type and use of this PPE appropriate?
1926.102(a)(1)
  ANSI Z87.1-1989

## Slide 7: Examples of Eye and Face Protection
Eye and face protection
NCDOL Photo Library
Safety Goggles
Welding
Helmet
NCDOL Photo Library
NCDOL Photo Library
ANSI/ISEA Z87.1
Safety Glasses

## Slide 8: Any other hazards?
NCDOL PHOTO LIBRARY
Ventilation
Noise
UV/IR rays
Metal fumes

## Slide 9: Fall Protection
    The date(s) of the training, and the signature of the person who conducted the training, or the signature of the employer.
NCDOL Photo Library
Number 3: Certification of Training
  Employer must verify fall protection training by preparing a written certification record.
  Record shall contain the name or other identity of the employee trained.
1926.503(b)(1)

## Slide 10: Portable Ladders
Number 4: Ladders
  When portable ladders are used for access to an upper landing surface, they must:
    Extend 3 feet above landing.
    Be properly secured at the top
    with a grasping device provided
    (such as a grab rail).
1926.503(b)(1)

## Slide 11: Portable Ladders
Portable ladder not extended at least 3 feet above upper landing surface.
1926.503(b)(1)

## Slide 12: Portable Ladders
Portable ladder not extended at least 3 feet above upper landing surface.
NCDOL Photo Library
1926.503(b)(1)

## Slide 13: Personal Protective Equipment
1926.100(a)
    Protective helmets must comply with:
        ANSI Z89.1-2009
        ANSI Z89.1-2003
        ANSI Z89.1-1997
Number 5: Head Protection - General Requirements
  Employees working in areas where there is a possible danger of head injury from impact, or from falling or flying objects, or from electrical shock and burns, must be protected by protective helmets.

## Slide 14: Head Protection
Head Protection - General Requirements
  Is there a possible danger to the head from an impact, or from falling or flying objects, or from electrical shock and burns?
1926.100(a)
NCDOL Photo Library

## Slide 15: General Safety and Health Provisions
Number 6: Accident Prevention Responsibilities
  Provide for frequent and regular inspections of job sites, materials, and equipment to be made by competent persons designated by employers.
1926.20(b)(2)
NCDOL Photo Library
NCDOL Photo Library

## Slide 16: Fall Protection
Number 7: Training Program
  Employer must provide a training program for each employee who might be exposed to fall hazards.
1926.503(a)(1)
NCDOL Photo Library
NCDOL Photo Library

## Slide 17: Fall Protection
Employees must know:
  How to properly wear equipment
  Where to tie off
1926.503(a)(2)
NCDOL Photo Library
NCDOL Photo Library

## Slide 18: Fall Protection
Is equipment inspected and properly maintained?
1926.503(a)(2)
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library

## Slide 19: Stairways and Ladders Usage
Number 8: Self-supporting top (top cap) or top step must not be used as a step.
1926.1053(b)(13)
NCDOL Photo Library
NCDOL Photo Library

## Slide 20: Stairways and Ladders Usage
Number 9: Stairways and ladders - Employer must provide a training program for each employee using ladders and stairways.
  Competent person
    Nature of fall hazards in the work area;
    Correct procedures for erecting, maintaining, and disassembling the fall protection systems to be used;
    Proper construction, use, placement, and care in handling of all stairways and ladders; and
    Maximum intended load-carrying capacities of ladders used.
1926.1060(a)

## Slide 21: Competent Person
A "competent person" is defined as one who is capable of identifying existing and predictable hazards in the surroundings or working conditions,
1926.32(f)
NCDOL Photo Library
  Which are unsanitary, hazardous, or dangerous to employees, and who has authorization to take prompt corrective measures to eliminate them.

## Slide 22: Portable Ladders
Number 10: Used only for designed purpose - Ladders shall be used only for the purpose for which they were designed.
1926.1053(b)(4)

## Slide 23
Hazard Recognition in the Construction Industry

## Slide 24: Hazard Recognition
1926.501(b)(1)
Circular saw
NCDOL Photo Library
Notes: 24

## Slide 25: Hazard Recognition
1926.501(b)(1)
NCDOL Photo Library
Anchor
Lanyard
Notes: them. (1910.501(b)(2)
25

## Slide 26: Hazard Recognition
NCGS 95-129
NCDOL Photo Library
Impalement
hazard
NCDOL Photo Library
Notes: 26

## Slide 27: Hazard Recognition
1926.1053(b)(13)
Using the top of the ladder
Employees
NCDOL Photo Library
Notes: 27

## Slide 28: Hazard Recognition
1926.1053(b)(1)
1926.1053(b)(4)
Ladder hazards
NCDOL Photo Library
Notes: 28

## Slide 29: Hazard Recognition
1926.96
1926.102
1926.501(b)(13)
No eye protection
NCDOL Photo Library
No protective footwear
Notes: 29

## Slide 30: Hazard Recognition
1926.250(c)
Notes: 30

## Slide 31: Hazard Recognition
1926.403(b)(2)
1926.404
No ground - bypassed
Listed and labeled
NCDOL Photo Library
NCDOL Photo Library
Notes: 31

## Slide 32: Hazard Recognition
No fall protection
> 20 ft elevation
NCDOL Photo Library
1926.501(b)(13)

## Slide 33: What’s the Hazard?
No fall protection
One hand must grasp ladder
NCDOL Photo Library
1926.501(b)(13)
1926.1053(b)(21) – (22)

## Slide 34: Summary
In this course, we discussed the Top Ten most frequently cited serious Construction Industry violations for FFY 2022.
  You should now understand and be able to identify hazards associated with the Top Ten most cited serious OSH violations in the Construction Industry.

## Slide 35: Thank You For Attending!
Final Questions?