## Slide 1: Top 10 Most Frequently Cited Serious Violations in FFY 2023
Presented by:
29 CFR 1926 - Construction
Notes: Revised: 06/06/24
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education, Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.
The data is Federal Fiscal Year (explained on next page).

## Slide 2: Objectives
In this course, we will discuss the Top Ten most frequently cited serious Construction Industry violations for federal fiscal year (FFY) 2023.
NCDOL Photo Library
Citations and violations issued from 10/01/2022, through 09/30/2023, in North Carolina.
NCDOL Photo Library

## Slide 3: Fall Protection
Number 1: Residential Construction
  Each employee engaged in residential construction activities 6 feet (1.8 m) or more above lower levels shall be protected.
1926.501(b)(13)
    Personal fall arrest system
    Guardrail systems
    Safety net system

## Slide 4: Fall Protection
Where is fall protection required?
1926.501(b)(13)
NCDOL Photo Library
NCDOL Photo Library

## Slide 5: Personal Protective Equipment
Number 2: Eye and Face Protection - General Requirements
  Provide employees with eye and face protection when machines or operations present potential eye or face injury from physical, chemical, or radiation agents.
1926.102(a)(1)

## Slide 6: Eye and Face Protection
Is the type and use of this PPE appropriate?
  ANSI Z87.1-1989
1926.102(a)(1)

## Slide 7: Examples of Eye and Face Protection
Eye and face protection
NCDOL Photo Library
ANSI/ISEA Z87.1
Safety Glasses
NCDOL Photo Library
Safety Goggles
Welding
Helmet
NCDOL Photo Library

## Slide 8: Any other hazards?
Ventilation
Noise
UV/IR rays
Metal fumes
NCDOL PHOTO LIBRARY

## Slide 9: Fall Protection
Number 3: Certification of Training
  Employer must verify fall protection training by preparing a written certification record.
  Record shall contain the name or other identity of the employee trained.
1926.503(b)(1)
NCDOL Photo Library
    The date(s) of the training, and the signature of the person who conducted the training, or the signature of the employer.
Notes: 9

## Slide 10: Portable Ladders
Number 4: Ladders
  When portable ladders are used for access to an upper landing surface, they must:
    Extend 3 feet above landing.
    Be properly secured at the top
    with a grasping device provided
    (such as a grab rail).
1926.1053(b)(1)
LOI – 1926.1053(b)(1)

## Slide 11: Portable Ladders
Portable ladder not extended at least 3 feet above upper landing surface.
1926.1053(b)(1)
Notes: 11

## Slide 12: Portable Ladders
Portable ladder not extended at least 3 feet above upper landing surface.
1926.1053(b)(1)
NCDOL Photo Library
Notes: 12

## Slide 13: Personal Protective Equipment
Number 5: Head Protection - General Requirements
  Employees working in areas where there is a possible danger of head injury from impact, or from falling or flying objects, or from electrical shock and burns, must be protected by protective helmets.
1926.100(a)
    Protective helmets must comply with:
        ANSI Z89.1-2009
        ANSI Z89.1-2003
        ANSI Z89.1-1997

## Slide 14: Head Protection
Head Protection - General Requirements
  Is there a possible danger to the head from an impact, or from falling or flying objects, or from electrical shock and burns?
1926.100(a)
NCDOL Photo Library

## Slide 15: General Safety and Health Provisions
Number 6: Accident Prevention Responsibilities
  Provide for frequent and regular inspections of job sites, materials, and equipment to be made by competent persons designated by employers.
1926.20(b)(2)
NCDOL Photo Library
NCDOL Photo Library

## Slide 16: Fall Protection
Number 7: Training Program
  Employer must provide a training program for each employee who might be exposed to fall hazards.
1926.503(a)(1)
NCDOL Photo Library
NCDOL Photo Library
Notes: 16

## Slide 17: Fall Protection
Employees must know:
  How to properly wear equipment
  Where to tie off
1926.503(a)(2)
NCDOL Photo Library
NCDOL Photo Library
Notes: 17

## Slide 18: Fall Protection
Is equipment inspected and properly maintained?
1926.503(a)(2)
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library
Notes: 18

## Slide 19: Stairways and Ladders Usage
Number 8: Self-supporting top (top cap) or top step must not be used as a step.
1926.1053(b)(13)
NCDOL Photo Library
NCDOL Photo Library

## Slide 20: Respirable Crystalline Silica
1926.1153(c)(1)
Number 9: Exposure control methods must be implemented as required.
  Refer to Table 1 for specified methods

## Slide 21: Controls Not Functioning Properly

## Slide 22: Example of Table 1
1926.1153(c)(1)
Equipment/Task | Engineering and work practice control methods | Required respiratory protection and minimum assigned protection factor (APF) | 
 |  | ≤ 4 hours/shift | > 4 hours/shift
(i) Stationary masonry saws | Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions. | None | None
Table 1 – Specified Exposure Control Methods When Working With Materials Containing Crystalline Silica

## Slide 23: Fall Protection
Number 10: Unprotected Sides and Edges
  Each employee on a walking/working surface (horizontal and vertical) with an unprotected side or edge which is 6 feet (1.8m) or more above a lower level
1926.501(b)(1)
NCDOL Photo Library
    Guardrail systems with toe-boards
    Safety net systems
    Personal fall arrest systems

## Slide 24: Lack of Fall Protection
1926.501(b)(1)
NCDOL Photo Library
NCDOL Photo Library

## Slide 25: Hazard Recognition in the Construction Industry

## Slide 26: Hazard Recognition
1926.501(b)(1)
Circular saw
NCDOL Photo Library
Notes: 26

## Slide 27: Hazard Recognition
1926.501(b)(1)
NCDOL Photo Library
Anchor
Lanyard
Notes: 27

## Slide 28: Hazard Recognition
NCGS 95-129
NCDOL Photo Library
Impalement
hazard
NCDOL Photo Library
Notes: 28

## Slide 29: Hazard Recognition
1926.1053(b)(13)
Using the top of the ladder
Employees
NCDOL Photo Library
Notes: 29

## Slide 30: Hazard Recognition
1926.1053(b)(1)
1926.1053(b)(4)
Ladder hazards
NCDOL Photo Library
Notes: 30

## Slide 31: Hazard Recognition
1926.96
1926.102
1926.501(b)(13)
No eye protection
NCDOL Photo Library
No protective footwear
Notes: 31

## Slide 32: Hazard Recognition
1926.250(c)
Notes: 32

## Slide 33: Hazard Recognition
1926.403(b)(2)
1926.404
No ground - bypassed
Listed and labeled
NCDOL Photo Library
NCDOL Photo Library
Notes: 33

## Slide 34: Hazard Recognition
No fall protection
> 20 ft elevation
NCDOL Photo Library
1926.501(b)(13)

## Slide 35: What’s the Hazard?
No fall protection
One hand must grasp ladder
NCDOL Photo Library
1926.501(b)(13)
1926.1053(b)(21) – (22)

## Slide 36: Summary
In this course, we discussed the Top Ten most frequently cited serious Construction Industry violations for FFY 2023.
  You should now understand and be able to identify hazards associated with the Top Ten most cited serious OSH violations in the Construction Industry.

## Slide 37: Thank You For Attending!
Final Questions?