## Slide 1: Chainsaw Safety
29 CFR 1910.266
Notes: Revised 06/16/25
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
At the end of this course, students will:
  Understand relevant definitions
  Know appropriate PPE for chainsaw activities
  Be able to recognize basic chainsaw hazards
  Understand the basics of chainsaw safety
  Understand training requirements
29 CFR 1910.266

## Slide 3: Definitions
Backcut (felling cut)
  Final cut in a felling operation.
Bucking
  Sawing felled trees into sections called logs.
Danger tree
  Standing tree that presents a hazard to employees due to deterioration or physical damage to the root system, trunk, stem or limbs, and the direction and lean of the tree.
1910.266(c)

## Slide 4: Definitions
Limbing
  To cut branches off felled trees.
Logging operations
  Operations associated with felling and moving trees and logs from the stump to the point of delivery.
Spring pole
  A tree, segment of a tree, limb, or sapling under stress or tension due to pressure or weight of another object.
1910.266(c)

## Slide 5: Definitions
Undercut
  A notch cut in a tree to guide the direction of the tree fall and to prevent splitting or kickback.
Yarding
  Movement of logs from the place they are felled to a landing.
1910.266(c)

## Slide 6: Felling Trees
More people are killed while felling trees than during any other logging activity.
“Barber chair”

## Slide 7
Chainsaw Operator Injuries

## Slide 8: Personal Protective Equipment
PPE must be inspected prior to use on each workshift to ensure it is in serviceable condition.
PPE must be used when hazards make it necessary.
  Except for foot protection, all PPE must be provided by the employer at no cost to the employee.
1910.266(d)(1)

## Slide 9: Personal Equipment Checklist
Hand protection if handling wire rope
Leg protection
Foot protection
Head protection
Eye and face protection
Hearing protection
First aid kits

## Slide 10: Hand Protection
Employees who handle wire rope are required to wear hand protection that protects against puncture wounds, cuts, and lacerations.
1910.266(d)(1)(iii)

## Slide 11: Leg Protection
Each employee who operates a chainsaw must wear leg protection constructed with cut-resistant material.
1910.266(d)(1)(iv)

## Slide 12: Leg Protection
1910.266(d)(1)(iv)

## Slide 13: Foot Protection
Foot protection that is constructed with cut-resistant material.
1910.266(d)(1)(v)

## Slide 14: Head Protection
Hard hats must be worn when overhead hazards are present.
1910.266(d)(1)(vi)

## Slide 15: Eye and Face Protection
Eye and face protection must be worn where there is potential for injury to the eyes or face.
1910.266(d)(1)(vii)

## Slide 16: Hearing Protection
1910.95
When employees are exposed to sound exceeding levels in Table G-16 (below), feasible administrative or engineering controls shall be utilized.
  If controls fail to reduce sound levels, hearing protections shall be provided.
Duration (hours per day) | dBA
8 | 90
6 | 92
4 | 95
3 | 97
2 | 100
1 ½ | 102
1 | 105
½ | 110
¼ or less | 115

## Slide 17: Good, but could it be better?

## Slide 18: First Aid Kits
Provided at each work site where trees are being cut.
Number and contents of each kit shall reflect the degree of isolation, number of employees, and hazards reasonably anticipated at work site.
  Appendix A
  Maintained in serviceable
  condition
1910.266(d)(2)

## Slide 19: Signaling and Signal Equipment
Hand signals or audible contact utilized whenever factors prevent clear understanding of voice communications between employees.
Only a designated person gives signals, except in an emergency.
1910.266(d)(7)

## Slide 20: Flammable and Combustible Liquids
Flammable and combustible liquids shall be stored, handled, transported, and used in accordance with the requirements of 1910.106.
Flammable and combustible liquids shall not be transported in the driver compartment or in any passenger-occupied area of a machine or vehicle.
1910.266(d)(9)

## Slide 21: Chainsaw Checklist
Chain brake
Throttle interlock
Chain catcher
Chain tension
Muffler
Chainsaw kickback
Chain sharpness, cutter shape, depth usage setting,
lubrication
Handles and guards on tight
No chain movement when engine is idling
1910.266(e)(1)-(2)

## Slide 22: Chainsaw Mechanisms
1. Chain catcher – prevents a broken or dislodged chain from striking the logger
2. Flywheel
3. Clutch
4. Decompression valve
5./7. Anti-vibration handle system – recommended by OSHA to limit ergonomic stress to logger’s joints
1910.266(e)(2)

## Slide 23: Chainsaw Mechanisms
6. Hand guard
8. Muffler to reduce engine noise
9. Chain brake – stops chain if kickback occurs (if saw was placed into service after 2/9/95)
10. Throttle – will stop chain when
pressure on throttle is released
11. Throttle interlock – prevents
throttle from activating until
interlock is depressed
1910.266(e)(2)

## Slide 24: Before Starting the Saw
Chainsaw fueled at least 10 feet from sources of ignition.
Fuel container should meet the following requirements identified in 1910.266(d)(9):
  Must be metal or plastic.
  Must not exceed a 5-gallon capacity.
  Must be approved by the Underwriters Laboratory (UL), Factory Mutual (FM), the Department of Transportation (DOT), or other Nationally Recognized Testing
  Laboratory (NRTL).
1910.266(e)(2)

## Slide 25: Before Starting the Saw
Controls, chain tension, and all bolts and handles checked to ensure they are functioning properly and adjusted according to the manufacturer's instructions.
Chainsaw started at least 10 feet from fueling area, with chain brake engaged, and with chainsaw on the ground or otherwise firmly supported.
1910.266(e)(2)

## Slide 26: While Running the Saw
Both hands on the handles
Secure footing maintained
Obstacles cleared that interfere with cutting the tree or retreating
Chainsaw should not be used above shoulder level
1910.266(e)(2)

## Slide 27: While Running the Saw
Throttle released, chain brake on prior to retreating
Chainsaw is off or chain brake engaged whenever it’s carried more than two steps or on hazardous terrain
1910.266(e)(2)

## Slide 28: Manual Felling
Potential hazards eliminated or minimized
Felling direction determined
Retreat path planned and cleared
Hinge size determined
Proper felling techniques used
1910.266(h)(2)

## Slide 29
Eliminate/Minimize Hazards
1910.266(h)(2)
Primary hazards include unstable logs and hazards associated with using chainsaws.
Prior to limbing, the following is evaluated:
  Overhead hazards
  Butt movement forward
  Butt twist
  Butt off the ground
  “Danger trees”

## Slide 30
Limbing and bucking shall be done on the uphill side of each tree or log on any slope where rolling or sliding of trees or logs is reasonably foreseeable.
Loggers should never limb a tree immediately after felling.
Good idea to drop several trees and then refuel the saw prior to limbing.
  Provides time for overhead hazards to come down.
Limbing and Bucking
1910.266(h)(3)

## Slide 31: “Danger Trees"
Lodged trees
Entangled trees
1910.266(h)
“Lodged Trees”

## Slide 32: “Danger Trees"
Spring poles
Dead trees/limbs
Stalled trees
1910.266(h)

## Slide 33: “Dutchman Cut"

## Slide 34: Felling Direction
Clear fall path
  A clear fall path is an important factor in deciding what direction to fell a tree.
  Fall path should be visualized in all directions and identify those directions that are free of other trees.
  Finding a clear path will eliminate lodged trees, throwback, and damage to the tree being felled as well as the other trees.
1910.266(h)(2)

## Slide 35: Felling Direction
Clear landing
  Felling a tree onto stumps, large rocks, or uneven ground should be avoided.
    This will prevent or reduce cracking and other damage to the tree, and limit the potential for rebound of the tree.
Lean of tree
  Generally easier and safer to fell a tree in direction that it is already leaning.
    This makes for a cleaner fall and eliminates the need to use wedges, allowing gravity to do the work.
1910.266(h)(2)

## Slide 36: Felling Direction
Ease of removal
  When possible, the butt of felled tree should face the skid road, and tree consistent with felling pattern of other trees.
    Makes for efficient limbing and removal.
Slope of ground
  Fell in direction that will minimize chance the tree will roll/slide.
1910.266(h)(2)

## Slide 37
1910.266(h)(2)
Felling Direction

## Slide 38: Retreat Path
Before felling is started, the feller shall plan and clear a retreat path.
Retreat path shall extend diagonally away from the expected felling line unless the employer demonstrates that such a retreat path poses a greater hazard than an alternate path.
Once the backcut has been made the feller shall immediately move a safe distance away from the tree on the retreat path.
1910.266(h)(2)(i)

## Slide 39: Retreat Path
1910.266(h)(2)(i)

## Slide 40: Hinge Size
Hinge length should be 80% of the diameter of the tree at breast height.
Hinge width should be 10% of the diameter of the tree at breast height.
Hinge on a tree with no side lean should be perpendicular to the intended direction of fall.
1910.266(h)(2)(vi)

## Slide 41: Felling Techniques
Backcut
  Shall be made in each tree being felled.
  Shall leave sufficient hinge wood to hold tree to stump during most of its fall so hinge is able to guide the tree's fall in intended direction.
  Shall be above level of horizontal facecut in order to provide an adequate platform to prevent kickback.
    Exception: Backcut may be at or below horizontal facecut in tree pulling operations.
    Requirement does not apply to open face felling where two angled facecuts rather than a horizontal facecut are used.
1910.266(h)(2)(v)-(vii)

## Slide 42: Felling Techniques
Undercut
  Shall be made in each tree being felled unless the employer demonstrates that felling the tree without an undercut will not create a hazard for an employee.
  Shall be of a size so the tree will not split and will fall in the intended direction.
1910.266(h)(2)(v)-(vii)

## Slide 43: Type of Cuts

## Slide 44: Types of Notches

## Slide 45
Does this cut look correct?

## Slide 46
Does this cut look correct?

## Slide 47
Is he cutting correctly?

## Slide 48: Training
Frequency
  Prior to initial assignment
  Whenever assigned new tasks, tools, equipment, machines, or vehicles
  Employee demonstrates unsafe job performance
1910.266(i)(2)

## Slide 49: Training
Content
  Safe performance of assigned work tasks
  Recognition of safety and health hazards
  Procedures, practices and requirements of the employer's work site
  Requirements of this standard
1910.266(i)(3)

## Slide 50: Training
Employer must ensure that each employee can properly and safely perform the work tasks and operate tools, equipment, machines, and vehicles used in their job.
Each employee shall work under the close supervision of a designated person until employee demonstrates the ability to safely perform their new duties independently.
1910.266(i)(5) – (6)

## Slide 51: Training
First aid training
  Employer shall assure each employee, including supervisors, receives or has received first aid and CPR training.
  Employer shall assure each employee's first aid and CPR training and/or certificate of training remain current.
1910.266(i)(7)

## Slide 52: Training
Training conducted by a designated person.
Training presented in a manner that employee is able to understand.
Written certification record
1910.266(i)(8)-(10)

## Slide 53: Summary
In this course, we discussed:
  Definitions
  Personal protective equipment
  Hazards
  Chainsaw safety
  Training

## Slide 54: Thank You For Attending!
Final Questions?