## Slide 1: Concrete and Masonry in Construction
Subpart Q
Presented by:
Notes: Revised 11/2017
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
  In this course, we will discuss the following:
    OSHA’s minimum requirements for concrete and masonry work in construction
    General requirements, equipment, tools, formwork, shoring, precast concrete, and lift-slab operations
    Hazards associated with concrete and masonry construction operations
    Abatement methods
NCDOL Photo Library

## Slide 3: Subpart Q – Concrete and Masonry Construction
1926.700 – Scope, application, and definitions
1926.701 – General requirements
1926.702 – Requirements for equipment and tools
1926.703 – Requirements for cast-in-place concrete
1926.704 – Requirements for precast concrete
1926.705 – Requirements for lift slab operations
1926.706 – Requirements for masonry construction

## Slide 4: Definitions
Bull float
  A tool used to spread out and smooth concrete
Formwork
  The total system of support for freshly placed or partially cured concrete
Lift slab
  A method of concrete construction in which floor and roof slabs are cast on or at ground level and, using jacks, lifted into position
1926.700(b)
NCDOL Photo Library

## Slide 5: Definitions
Limited access zone
  An area alongside a masonry wall, which is under construction, and is clearly demarcated to limit access by employees
Precast concrete
  Concrete members which have been formed, cast, and cured prior to final placement in a structure
Reshoring
  Construction operation in which shoring equipment is placed, as original forms and shores are removed, to support partially cured concrete and construction loads
1926.700(b)
Limited access zone
NCDOL Photo Library

## Slide 6: Definitions
Shore
  A supporting member that resists a compressive force imposed by a load
Vertical slipforms
  These forms are jacked vertically during placement of concrete
Jacking operation
  Task of lifting a slab during the construction of a building where the lift-slab process is being used
1926.700(b)

## Slide 7: Does Subpart Q Apply?

## Slide 8: Construction Loads
Structures must be capable of supporting loads
1926.701(a)
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library

## Slide 9: Reinforcing Steel
Guard protruding, reinforcing steel
  Letter of interpretation: 05/29/1997
    Addresses use of small plastic rebar caps
  Letter of interpretation: 03/10/2006
    Horizontal protection from impalement
1926.701(b)
NCDOL Photo Library

## Slide 10: Post-Tensioning Operations
Method of reinforcing concrete, masonry, and other structural elements
Strands ½″ diameter are stressed to a force of 33,000 lbs. using a hydraulic jack
1926.701(c)
NCDOL Photo Library

## Slide 11: Post-Tensioning Operations
No non-essential employees allowed in hazard zone
Use signs and barriers to limit employees access to work zone
1926.701(c)(1)-(2)
NCDOL Photo Library

## Slide 12: Riding Concrete Buckets
1926.701(d)
No riders

## Slide 13: Working Under Loads
Employees must not be permitted under concrete buckets while they are being elevated or lowered into position
1926.701(e)(1)
NCDOL Photo Library

## Slide 14: Working Under Loads
Elevated concrete bucket routes
1926.701(e)(2)
NCDOL Photo Library

## Slide 15: Personal Protective Equipment
Employees must wear protective head and face equipment when applying cement, sand, and water mixture through a pneumatic hose
1926.701(f)

## Slide 16: Bulk Cement Storage
Bins, containers, and silos must be equipped with:
  Conical or tapered bottoms
  Mechanical or pneumatic
  means to start flow of
  material
Ejection system must be
shut down, locked and
tagged out prior to entry
1926.702(a)(1)-(2)

## Slide 17: Concrete Mixers
Concrete mixers with one cubic yard or larger loading skips must be equipped with:
  Mechanical device to clear skip of materials
  Guardrails installed on each side of the skip
1926.702(b)(1)-(2)

## Slide 18: Power Concrete Trowels
Manually guided concrete troweling machine must be equipped with:
  Automatic control switches shut off power when hands are removed
1926.702(c)
NCDOL Photo Library
NCDOL Photo Library

## Slide 19: Concrete Buggy
Concrete buggy handles must not extend beyond the wheels on either side of the buggy
1926.702(d)
NCDOL Photo Library

## Slide 20: Concrete Pumping System
Discharge pipes must be provided with pipe supports designed for 100 percent overload
Compressed air hoses must be provided with positive fail-safe joint connectors
1926.702(e)(1)-(2)
NCDOL Photo Library

## Slide 21: Concrete Buckets
Concrete buckets equipped with hydraulic or pneumatic gates:
  Must have positive safety latches or similar devices to prevent accidental dumping
  Designed to prevent concrete
  from hanging up on top and
  sides
1926.702(f)(1)-(2)

## Slide 22: Tremies
Sections of tremie and similar concrete conveyances must be secured with wire rope (or equivalent materials) in addition to the regular couplings or connections
1926.702(g)

## Slide 23: Bull Floats
Bull float handles must be constructed of nonconductive material or insulated
  When used where they may contact energized electrical conductors
1926.702(h)

## Slide 24: Masonry Saws
Masonry saws must be guarded with a semicircular enclosure over the blade
Method for retaining blade fragments must be incorporated in the
design of the enclosure
1926.702(i)(1)-(2)

## Slide 25: Lockout/Tagout Procedures
Employees must not be allowed to perform maintenance or repair activity on equipment
  Unless hazardous energy sources have locked out or tagged out
1926.702(j)(1)

## Slide 26: General Requirements
Formwork must be designed, fabricated, erected, supported, braced, and maintained
  Must support, without failure, all vertical and lateral loads applied to it
1926.703(a)(1)
NCDOL Photo Library

## Slide 27: General Requirements
Drawings or plans for the jack layout, formwork, working decks, and scaffolds must be available at the jobsite
1926.703(a)(2)
NCDOL Photo Library

## Slide 28: Shoring and Reshoring
Inspected prior to erection
Damaged equipment shall not be used
Inspected immediately prior to, during, and
immediately after concrete placement
1926.703(b)(1)-(3)

## Slide 29: Shoring and Reshoring
Equipment found to be damaged or weakened must be immediately reinforced
Sills must be sound, rigid, and capable of carrying maximum intended load
1926.703(b)(4)-(5)

## Slide 30: Shoring and Reshoring
All base plates, shore heads, extension devices, and adjustment screws must be in firm contact, and secured when necessary, with the foundation and the form
1926.703(b)(6)
NCDOL Photo Library
NCDOL Photo Library

## Slide 31: Shoring and Reshoring
Adjustment of single post shores to raise formwork must not be made after the placement of concrete
1926.703(b)(9)
NCDOL Photo Library

## Slide 32: Shoring and Reshoring
Reshoring must be erected:
  As the original forms and shores are removed
  Whenever the concrete is required to support loads in excess of its capacity
1926.703(b)(10)
NCDOL Photo Library

## Slide 33: Vertical Slipforms
Form steel rods or pipes on which jacks climb must be:
  Designed for that purpose and adequately braced when not encased in concrete
  Provided with scaffolds or work platform where
  employees required to pass
1926.703(c)(1)-(3)
NCDOL Photo Library
NCDOL Photo Library

## Slide 34: Vertical Slipforms
Jacks and lifting devices must be provided with mechanical dogs or other automatic holding devices
1926.703(c)(5)
NCDOL Photo Library
NCDOL Photo Library

## Slide 35: Removal of Formwork
Forms and shores must not be removed until employer determines concrete has gained sufficient strength
1926.703(e)(1)
NCDOL Photo Library

## Slide 36: Precast Concrete
Wall units, structural framing, and tilt-up wall panels must be adequately supported to prevent overturning
1926.704(a)

## Slide 37: Precast Concrete
Tilt-up precast concrete members
  Lifting inserts embedded or otherwise attached must be capable of supporting at least two times the maximum intended load
Precast concrete members (other than tilt-up members)
  Lifting inserts capable of supporting at
  least four times maximum intended
  load
1926.704(b) - (c)
NCDOL Photo Library
NCDOL Photo Library

## Slide 38: Precast Concrete
Lifting hardware must be capable of supporting at least five times maximum intended load
1926.704(d)
NCDOL Photo Library

## Slide 39: Precast Concrete
No employees permitted under precast concrete members being lifted or tilted into position
  Except employees required
  for the erection of those members
1926.704(e)
NCDOL Photo Library

## Slide 40: Fall Protection
Each employee engaged in the erection of precast concrete members and related operations who is 6 feet or more above lower levels shall be protected from falling
1926.501(b)(12)
NCDOL Photo Library

## Slide 41: Precast Concrete
Precast walls can be installed quickly
Foundations can be backfilled as soon as the slab is in placed, enhancing jobsite safety

## Slide 42: Lift-Slab Operations
Designed by a registered professional engineer
Plans and designs implemented by employer must include:
  Detailed instructions
  Sketches indicating method of
  erection
1926.705(a)
Simulating Hydraulic Jacks
NCDOL Photo Library

## Slide 43: Jack/Lifting Unit
Marked to indicate rated capacity
Not loaded beyond capacity
Synchronized lifting to ensure uniform lifting
Manual controls located in central location—attended by competent person (must be experienced)
No employees permitted in the building or structure while any jacking operation is taking place
  Except essential personnel
1926.705(b), (c), (g), (i),(k)(1)
NCDOL Photo Library

## Slide 44: Limited Access Zone
Established prior to the start of construction
Equal to the height of the wall plus four feet
Un-scaffolded side of wall
Restricted to entry by employees constructing the wall
Remain until adequately supported
1926.706(a)(1)-(5)
NCDOL Photo Library
Limited Access Zone

## Slide 45: Adequate Bracing
Masonry walls over 8 feet in height must be adequately braced
Bracing must remain in place until permanent supporting elements of the structure are in
place
1926.706(b)
NCDOL Photo Library
NCDOL Photo Library

## Slide 46: Adequate Bracing

## Slide 47: Summary
We covered the following information:
  OSHA’s minimum requirements for concrete and masonry work in construction
  General requirements for equipment, tools, formwork, shoring, precast concrete, and lift-slab operations
  Hazards associated with
  concrete and masonry
  construction operations
  Abatement methods
NCDOL Photo Library
Notes: 47

## Slide 48: Thank You For Attending!
Final Questions?