## Slide 1: Fall Protection in Construction
§1926 Subpart M
Notes: Revised : 6/16/25
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
After this course, students will:
Recognize fall hazards in construction
Understand Subpart M requirements
Be able to apply fall protection standards to construction
work sites

## Slide 3: Falls= 46% of CY 2018-2022 Construction Fatalities in North Carolina

## Slide 4: Subpart M – Fall Protection
Exception
  Covers all fall hazards except specific requirements
found in:
    Subpart L – Scaffolds
    Subpart R – Steel erection
    Subpart S – Tunneling operations
    Subpart V – Power transmission and distribution
    Subpart X – Stairways and ladders
    Subpart CC – Cranes and derricks
    13 NCAC 07F .0605 – Communication towers
1926.500-503

## Slide 5: Subpart M – Fall Protection
Exception
  The provisions of this subpart do not apply when employees are making an inspection, investigation, or assessment of workplace conditions prior to the actual start of construction work or after all construction work has been completed
1926.500(a)(1)

## Slide 6: Fall Exposure: Then and now...
1969 Construction
Est. fall exposure
  Drip edge = 11 feet
  Roof peak = 16 feet
2008 Construction
Est. fall exposure
  Drip edge = 23 feet
  Roof peak = 38 feet
NCDOL Photo Library
NCDOL Photo Library

## Slide 7: Fall Protection Requirements
General Industry
Construction
Scaffolds
Steel Erection
4′
6′
10′
15′

## Slide 8: Duty to Have Fall Protection 1926.501(a)
Employer required to provide fall protection systems
Employer must determine if the walking/working surfaces on which its employees are to work have the strength and structural integrity to support employees safely

## Slide 9: Fall Protection Required 1926.501(b)(1)-(15)
Overhand bricklaying
Low-slope roofs
Steep roofs
Pre-cast concrete erection
Residential construction
Wall openings
Other walking and working surfaces
Unprotected sides, edges
Leading edges
Hoist areas
Holes
Formwork, reinforcing steel
Ramps, runways
Excavations
Dangerous equipment

## Slide 10: Fall Protection Required
Unprotected sides and edges
1926.501(b)(1)

## Slide 11: Fall Protection Required
Leading edges
1926.501(b)(2)
NCDOL Photo Library

## Slide 12: Fall Protection Required
Hoist areas
1926.501(b)(3)
NCDOL Photo Library

## Slide 13: Fall Protection Required
Holes
  More than 6 feet above lower level
  Includes skylights
1926.501(b)(4)
NCDOL Photo Library
NCDOL Photo Library

## Slide 14: Fall Protection Required
Formwork and reinforcing steel
1926.501(b)(5)
NCDOL Photo Library

## Slide 15: Fall Protection Required
Ramps, runways, other walkways
1926.501(b)(6)
NCDOL Photo Library

## Slide 16: Fall Protection Required
Excavations
1926.501(b)(7)
NCDOL Photo Library

## Slide 17: Fall Protection Required
Dangerous equipment
1926.501(b)(8)
NCDOL Photo Library

## Slide 18: Fall Protection Required
Overhand bricklaying
1926.501(b)(9)
NCDOL Photo Library

## Slide 19: Fall Protection Required
Low-slope roof
  < 4/12 pitch
Steep roof
  > 4/12 pitch
1926.501(b)(10)-(11)
NCDOL Photo Library
NCDOL Photo Library

## Slide 20: Fall Protection Required
Residential construction
  STD 03-11-002 for citation guidance
1926.501(b)(13)

## Slide 21: Fall Protection Required
Wall openings
1926.501(b)(14)

## Slide 22: Falling Object
Each exposed employee must wear a hard hat
Employer must take steps to prevent employees from being hit by falling objects
  Erect toe boards, screens, or guardrail systems
  Erect a canopy structure
  Barricade the area
1926.501(c)

## Slide 23: Protection from Falling Objects
Toeboards
  When used as falling object protection, must be erected along the edge of the overhead walking/working surface
  Withstand force of at least 50 pounds
  Toeboards must be a minimum of 3½ inches in vertical height
1926.502(j)
NCDOL Photo Library

## Slide 24: Methods of Fall Protection
Conventional methods
  Safety nets
  Guardrails
  Personal fall arrest systems
1926.502(a)(1)
NCDOL Photo Library

## Slide 25: Guardrail System
NCDOL Photo Library
1926.502(b)

## Slide 26: Safety Nets
Used for:
  Bridges
  Demolition of multi-story buildings
Rarely used in residential construction
1926.502(c)

## Slide 27: Personal Fall Arrest System (PFAS)
NCDOL Photo Library

## Slide 28: Personal Fall Arrest System
Is this correct?

## Slide 29: Personal Fall Arrest System
D-Rings, snaphooks, lanyards, lifelines, anchorages rated @ 5,000 pounds
No free fall more than 6 feet; nor contact any lower level; 3.5 feet maximum deceleration
Provide for prompt rescue
Inspect prior to each use
1926.502(d)

## Slide 30: Personal Fall Arrest System
Body belts not allowed for fall arrest but may be used as a positioning device
Only locking type of snaphook can be used
1926.502(d)

## Slide 31: Methods of Fall Protection
Other acceptable methods
  Used under certain circumstances
    Warning lines
    Control access zones (CAZ)
    Safety monitor
    Fall protection plan
1926.502(f), (g), (h), (k)

## Slide 32: Warning Lines
Used on low-sloped roofs < 4/12
Erect 6 feet from all edges
Need fall protection for last 6 feet
Used in combination with other systems
Developed by competent person
1926.502(f),1926.501(b)(10)

## Slide 33: Controlled Access Zones
Used in:
  Leading edge work
  Overhand bricklaying
  Pre-cast concrete
Only authorized persons
NCDOL Photo Library
NCDOL Photo Library
1926.502(g)

## Slide 34: Safety Monitor System 1926.502(h)
Used on low-sloped roofs < 4/12
With roof widths < 50 feet, can use alone
Monitor must be competent person
  No other responsibilities

## Slide 35: Fall Protection Plan
Only for specific area or jobs
  Leading edge work
  Precast concrete erection work
  Residential construction work
Used when conventional fall protection equipment is infeasible or creates a greater hazard
Designed by qualified person
Supervised by competent person
1926.502(k)

## Slide 36: Covers for Holes
Covers must:
  Withstand two times weight of expected load
  Secured to prevent displacement
  Marked “hole” or “cover” or color-coded
NCDOL Photo Library
1926.502(i)

## Slide 37: Personal Fall Arrest System 1926.502(d)
Anchorage Connectors
Harness
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library

## Slide 38
NCDOL Photo Library
Personal Fall Arrest Systems

## Slide 39: Personal Fall Arrest Systems
Is this correct?

## Slide 40: Personal Fall Arrest Systems
Is this correct?

## Slide 41: Personal Fall Arrest Systems
Is this correct?

## Slide 42: Personal Fall Arrest Systems
Is this correct?

## Slide 43: Personal Fall Arrest Systems
Is this correct?

## Slide 44: Personal Fall Arrest Systems
Is this correct?

## Slide 45: Positioning Device System 1926.502(e)
Allows an employee to be supported on an elevated vertical surface
No more than 2 feet freefall
Inspected before each use
Safety belts okay for use

## Slide 46: Training Requirements 1926.503
Employer must:
  Provide a training program
  Ensure each employee has been trained
  Provide written certification of training
  Retrain where necessary
NCDOL Photo Library

## Slide 47: Summary
In this course, we discussed:
Fall hazards in construction
Subpart M requirements
Applying fall protection standards to construction sites

## Slide 48: Thank You For Attending!
Final Questions?