## Slide 1: Fire Protection – Portable Fire Extinguishers
29 CFR 1910.157
Notes: Revised: 6/16/25
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
In this course, we will discuss the following:
Scope and application
Exemptions
General requirements
Selection
Inspection and maintenance
Training
1910.157

## Slide 3: Scope and Application
Applies to the placement, use, maintenance, and testing of portable fire extinguishers provided for the use of employees
1910.157(a)

## Slide 4: Exemptions
Employer has established and implemented:
  Written fire safety policy
  Requires the immediate and total evacuation of employees
When extinguishers are not available
in the workplace, unless a specific
standard requires that a portable
fire extinguisher be provided
1910.157(b)(1)

## Slide 5: Exemptions
Employer exempt from the distribution requirements in paragraph (d) if employer has established and implemented:
  Emergency action plan that authorizes certain employees to use portable fire extinguishers
  Requires the immediate evacuation of all other employees
1910.157(b)(2)

## Slide 6: General Requirements
Employer shall:
  Provide portable fire extinguishers
  Mount, locate and identify them so they are readily accessible to employees without subjecting employees to possible injury
1910.157(c)(1)

## Slide 7: General Requirements
Only approved portable fire extinguishers shall be used
1910.157(c)(2)

## Slide 8: General Requirements
Employer shall not provide or make available in the workplace portable fire extinguishers using:
  Carbon tetrachloride, or
  Chlorobromomethane extinguishing agents
1910.157(c)(3)

## Slide 9: General Requirements
Employer shall assure:
  Fire extinguishers are maintained in a fully charged and operable condition
  Kept in their designated places at all times except during use
1910.157(c)(4)

## Slide 10: General Requirements
Employer shall remove the following fire extinguishers from service (delisted by Underwriters Laboratories in 1969):
  Soldered or riveted shell self-generating soda acid
  Self-generating foam
  Gas cartridge water type portable fire
  extinguishers which operate by being
  inverted
1910.157(c)(5)

## Slide 11: Selection and Distribution
Portable fire extinguishers shall be provided for employee use
Selected and distributed based on the classes of anticipated workplace fires, size and degree of hazard
1910.157(d)(1)

## Slide 12: Selection and Distribution
Employer shall distribute:
  Class A fire extinguishers within a travel distance of 75 feet or less
  Class A—Ordinary combustibles
    Wood
    Paper
    Plastic
    Cloth
    Rubber
1910.157(d)(2)

## Slide 13: Selection and Distribution
Employer may use:
  Uniformly spaced standpipe systems or hose stations connected to a sprinkler system instead of Class A fire extinguishers
    Systems must provide total coverage of area to be protected and employees must be trained annually in use
1910.157(d)(3)

## Slide 14: Selection and Distribution
Employer shall distribute:
  Class B fire extinguishers within a travel distance of 50 feet or less
    Class B—Flammable liquids
1910.157(d)(4)

## Slide 15: Selection and Distribution
Employer shall distribute:
  Class C fire extinguishers on the basis of the appropriate pattern for existing Class A or Class B hazards
    Class C—Electrical fires
1910.157(d)(5)

## Slide 16: Selection and Distribution
Employer shall distribute:
  Class D fire extinguishers within a travel distance of 75 feet or less
  Required in combustible metal areas where metal powders, flakes, and shavings are generated at least once every two weeks
    Class D—Metals
1910.157(d)(6)

## Slide 17: Inspection, Maintenance and Testing
Employer shall be responsible for the inspection, maintenance and testing of all portable fire extinguishers in the workplace
Fire extinguishers or hose shall be visually inspected monthly
1910.157(e)(1)-(2)

## Slide 18: Inspection, Maintenance and Testing
Employer shall:
  Assure that fire extinguishers are subjected to an annual maintenance check
  Record the annual maintenance date and retain record for one year
  Record available to the Assistant
  Secretary upon request
1910.157(e)(3)

## Slide 19: Inspection, Maintenance and Testing
Dry chemical extinguishers require a 12-year hydrostatic test
  Subjected to applicable maintenance procedures every 6 years
Exempted
  Dry chemical extinguishers having non-refillable
  disposable containers
1910.157(e)(4)

## Slide 20: Inspection, Maintenance and Testing
Employer shall assure that alternate equivalent protection is provided when portable fire extinguishers are removed from service for maintenance and recharging
1910.157(e)(5)

## Slide 21: Hydrostatic Testing
Employer shall assure that hydrostatic testing is performed by trained persons with suitable testing equipment and facilities
1910.157(f)(1)

## Slide 22: Hydrostatic Testing
Employer shall assure that portable extinguishers are hydrostatically tested at the intervals listed in Table L-1
Take this time to look up Table L-1
  29 CFR 1910.157(f)(2) Table L-1
  29 (Title)
    CFR (Code of Federal Regulations)
      1910 (Part)
        157 (f)(2) Table L-1 (Section)
Table L-1
1910.157(f)(2)

## Slide 23: Training and Education
Where employer has provided portable fire extinguishers for employee use
  Employer shall provide
  training on fire extinguisher
  use and hazards involved
  with incipient stage fire fighting
    Initially and annually thereafter
1910.157(g)(1)-(2)

## Slide 24: Training and Education
Employees who have been designated to use fire fighting equipment as part of an emergency action plan
  Employer shall provide training in use of appropriate equipment to designated group
    Initially and annually thereafter
1910.157(g)(3)-(4)

## Slide 25: Summary
In this course, we discussed:
Scope and application
Exemptions
General requirements
Selection
Inspection and maintenance
Training
1910.157

## Slide 26: Thank You For Attending!
Final Questions?