## Slide 1: Food Manufacturing Special Emphasis Program
NAICS 311
Presented by:
Notes: Revised: 08/30/2022
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
At the end of this course, students will understand:
  Purpose of a Food Manufacturing Special Emphasis Program (SEP).
  What this program means for North Carolina employers.
  Areas of focus when an inspection occurs.

## Slide 3: Why a Food Manufacturing SEP?
Employees exposed to production machinery.
Production jobs typically require no prior training and education.
Production levels are not sensitive to economic conditions.
Injury/illness rates higher than other sectors.

## Slide 4: Food Manufacturing
Industry groups:
NAICS 3111 Animal Food Mfg. | NAICS 3112 Grain and Oilseed Milling | NAICS 3113 Sugar and Confectionery Mfg. | NAICS 3114 Fruit and Vegetable Preserving and Specialty Food Mfg.
NAICS 3115 Dairy Product Mfg. | NAICS 3116 Animal Slaughtering and Processing | NAICS 3117 Seafood Product Prep and Packaging | NAICS 3118 Bakeries and Tortilla Mfg.
NAICS - North American Industry Classification System

## Slide 5: Bureau of Labor Statistics (BLS) Non-Fatal Incidence Rates
2020 BLS Data | TRC Rate | DART Rate
NC - All Private Industry | 2.2 | 1.3
National - All Private Industry | 2.9 | 1.8
NC - Food Manufacturing NAICS 311 | 3.8 | 3.0
National - Food Manufacturing NAICS 311 | 3.8 | 3.0
Total Recordable Case – TRC
Days Away, Restricted or Transferred – DART

## Slide 6: Inspection Types
Inspection assignments generated through:
  Fatalities
  Accidents
  Complaints and referrals
  General industry schedule criteria

## Slide 7: Inspection Priority
Inspections are generated and assigned according to priority.
  Imminent Danger > Fatality/Catastrophe > Complaints/Referrals > Follow-up/Monitoring > SEP Programmed
Unprogrammed inspections can be expanded to cover the SEP.

## Slide 8: Inspection Scope
Operational Procedure Notice 140 – Food Manufacturing SEP Inspection
Comprehensive Inspection
Complaint
OPN 140

## Slide 9: Focus Areas of SEP Inspection
Process Safety Management (PSM)
OSHA Recordkeeping/Medical Records
Combustible Dust
Confined Spaces
Machine Guarding
Electrical Hazards
Lockout-Tagout (LOTO)
Ergonomics
Hazard Communication
Other Hazards

## Slide 10: Machine Guarding
Focus Areas:

## Slide 11: Machine Guarding 1910.212(a)(1)
Guarding provided to protect employees from hazards created by:
  Point of operation
  Ingoing nip points
  Rotating parts
  Flying chips and sparks
Does this saw comply
with the requirement?

## Slide 12: Work Environment
Work often places employees in close proximity to moving equipment and systems.
Employee's access moving machinery to:
  Assist product flow,
  Clear blockages or spills, and
  Carry out cleaning duties.
Machine guarding required at the point of operation
1910 Subpart O

## Slide 13: General Requirements 1910.212(a)(3)
Machine guarding required at the point of operation.
Special hand-tools must be used when entering danger zone.
  Supplemental protection only

## Slide 14: Potential Hazard
Conveyors - Dangerous and deadly if insufficient guarding and if safety procedures are not enforced.
1910 Subpart O
  Examples:
    Materials placed correctly on conveyor.
    Employees trained to protect/safeguard hands.
    No long or loose clothing, hair, jewelry.

## Slide 15: Potential Hazard
Membrane skinners
  No guarding
  Severe damage and amputations can occur
1910 Subpart O
NCDOL Photo Library

## Slide 16: Potential Hazard
Overriding or circumventing guards
  Ensure guarding doesn’t hinder production.
  Ensure guarding can’t be circumvented.
1910.212(a)(3)(ii)
1910.212(a)(3)(ii) …The guarding device shall be in conformity with any appropriate standards therefor, or, in the absence of applicable specific standards, shall be so designed and constructed as to prevent the operator from having any part of his body in the danger zone during the operating cycle.

## Slide 17: Example Violation
Insufficient guarding/guarding not properly adjusted to cover the open blade.
  Exposing employees' hands to hazard
1910.212(a)(3)(ii)
NCDOL Photo Library

## Slide 18: Machine Guarding – Big Picture
Ensure effective barriers, covers, etc. are in place where needed.
Use LOTO when guarding must be circumvented.
Ensuring machine guarding reduces injuries.
Effective employee training.

## Slide 19: Electrical and Lockout/Tagout
Focus Areas:

## Slide 20: Electrical General Requirements
Examination installation, and use of equipment
  Electrical equipment must be free from recognized hazards:
    Cables exposed to sharp edges
    Splices
    Bare conductors
1910.303(b)(1)

## Slide 21: Electrical General Requirements
Installation and use
  Listed or labeled equipment shall be installed and used in accordance with its listing and labeling.
1910.303(b)(2)

## Slide 22: LOTO - Scope
Covers the servicing and/or maintenance of machines or equipment where the unexpected start-up or release of stored energy could cause injury.
  Installation and set-up
  Adjustment or maintenance
  Inspection
  Modification
  Routine service
1910.147(a)(1)
NCDOL Photo Library

## Slide 23: LOTO - Application
Normal production operations are not covered.
HOWEVER, servicing and/or maintenance tasks during production are covered if:
  Employee removes/bypasses guard or other safety device
  Employee is required to place any part of his/her body into the point of operation, or
  Where an associated danger zone exists during a machine operation.
1910.147(a)(2)

## Slide 24: LOTO - Application
Exception
  Minor tool changes and adjustments, and other minor servicing activities, which take place during normal production operations, are not covered if they are:
    Routine,
    Repetitive, and
    Integral to the use of the equipment for production
Provided that the work is performed using alternative measures which provide effective protection.
1910.147(a)(2)

## Slide 25: Energy Control Procedure
Energy control (LOTO) procedure
  Statement of intended use of procedure.
  Steps for shutting down, isolating, blocking and securing machines or equipment to control hazardous energy.
  Steps for the placement, removal and transfer of lockout devices or tagout devices and the responsibility for them, and
  Requirements for testing machine/equipment to determine and verify effectiveness of LOTO devices and other energy control measures.
1910.147(c)(4)

## Slide 26: Example Violation
Lack of effective training
  Common violation
  Examples:
    Employees, who were not qualified persons, were not trained in and familiar with any electrically related safety practices not specifically addressed by 29 CFR 1910.331 through 29 CFR 1910.335, but which were necessary for their safety.
    Employee was working from a ladder on a light fixture and experienced an electrical shock.
1910.332(b)(2)

## Slide 27: Hazard Communication
Focus Areas:

## Slide 28: Hazard Communication
Specific chemical hazards can include:
  Ammonia
  Chlorine
  Carbon dioxide
  Hydrogen peroxide
  Peracetic acid
NCDOL Photo Library

## Slide 29: Key Elements of HazCom
Hazard classification
Written program
Labeling
Safety data sheets (SDS)
Employee training
1910.1200

## Slide 30: Information and Training
Training topic requirements
  How to recognize a chemical presence or release
  Types of hazards chemicals present
  Hazards not otherwise classified (HNOC)
  How to protect themselves
  Parts hazard communication program:
    An explanation of the labeling system
    Safety data sheets
    How employees can obtain/use the appropriate hazard information
1910.1200(h)

## Slide 31: Hazard Example
Peracetic acid (PAA)
  Strong vinegar smell
  Irritating above 1 part per million (ppm)
  Corrosive and damaging to eyes and skin
  Respiratory irritant
  Level of hazard dependent on concentration

## Slide 32: Confined Space
Focus Areas:

## Slide 33: Confined Space
Many manufacturing sites contain permit-required confined spaces.
  Food manufacturing facilities often have a large number of confined spaces, such as silos, tanks, mixing vats and storage bins, which creates risks when maintenance is needed.
1910.146
NCDOL Photo Library

## Slide 34: Example Confined Spaces
Storage tanks
Process vessels
Boilers
Ducts
Utility vaults
Pipelines
Equipment and machinery
Open top spaces (>4 feet)
1910.146
NCDOL Photo Library

## Slide 35: Written Permit Space Program
If employees enter permit spaces, employer shall develop and implement a written permit space program.
1910.146(c)(4)
NCDOL Photo Library

## Slide 36: Combustible Dust
Focus Areas:

## Slide 37: Combustible Dust
Combustible dust is a risk factor in the manufacturing of numerous food product segments, such as:
    Bakery
    Cookie and cracker
    Snack food
    Blends/mixes
    Cereal
    Spices
CPL 03-00-008

## Slide 38: Combustible Dust
CPL 03-00-008
Any fine material that can catch fire and explode when mixed with air. Can be from:
  Most solid organic materials…
  Examples include sugar, starch, spices, flour
Can pass through a U.S. No. 40 Standard Sieve
  420 µm or smaller in diameter

## Slide 39: Combustible Dust
Multiple standards can apply:
  1910.22, Walking - Working Surfaces
    Must maintain sanitary conditions
  1910.38, Emergency Action Plans
  1910.94, Ventilation
  1910.146, Permit - Required Confined Spaces
  1910 Subpart L – Fire Protection
    For example: 1910.157, Portable Fire Extinguishers
  1910.307, Hazardous (classified) Locations
  1910.1200, Hazard Communication
CPL 03-00-008

## Slide 40: Elements of a Dust Explosion

## Slide 41: Combustible Dust
If combustible dust hazard are not controlled the results can be disastrous:
Dust explosions have been linked to numerous fatal accidents.
Between 1980 and 2005, the U.S. Chemical Safety Board investigated 281 combustible dust incidents that killed 119 workers and injured 718 others.
Example: 2/7/2008 - Imperial Sugar Refinery
  Large accumulations of sugar dust
  14 deaths, 38 injured
CPL 03-00-008

## Slide 42: Ergonomics
Focus Areas:

## Slide 43: Ergonomics
Definition
  Ergonomics is defined as the science related to man and his work, embodying the anatomic, physiologic, and mechanical principles affecting the efficient use of human energy.
Injury examples
  Carpal tunnel syndrome; tendinitis; rotator
  cuff injuries (a shoulder problem); epicondylitis
  (an elbow problem); trigger finger; muscle
  strains and lower back injuries.
NCGS 95-129(1)

## Slide 44: Ergonomic Program Elements
Management commitment
Employee involvement
Training
Workplace analysis
Prevention and control measures
Medical management
Program evaluation

## Slide 45: Movement/Environmental Stressors
Repetitive motions: Frequent and rapid muscular contractions
Static postures: In one position for long periods, reduces blood flow
Movement: Affected by work pace and task variety
Temperature: Psychological effects, hot, cold
Vibration: Damage small blood vessels and nerves

## Slide 46: Workplace Problems and Losses
Increased discomfort, pain, injury or illness
Workers’ compensation costs
Lost or restricted work time
Short- or long-term disability
Increased absenteeism
Greater turnover
Low morale
Decreased productivity and/or quality

## Slide 47: Hierarchy of Controls

## Slide 48: NCDOL OSH Division Perspective
North Carolina employers can be cited for ergonomic violations without an OSHA ergonomic standard.
Field Operations Manual (FOM) Chapter XVII
  Phase 1
  Phase 2
  Phase 3
Current citations are issued under the
General Duty Clause.

## Slide 49: Recordkeeping
Focus Areas:

## Slide 50: Recordkeeping – OPN 140
29 CFR 1904
Federal OSHA statistics have identified under-reporting of recordable cases in Food Manufacturing

## Slide 51: Who Must Record?
All employers in North Carolina except:
  Any employer with 10 or fewer employees for the previous calendar year.
  Any employer who is listed in the updated NAICS industry code list.
Exemptions above do not change employers’ reporting requirements.
1904.1

## Slide 52: General Recording Criteria
Death
Days away from work
Restricted work or transfer to another job
Medical treatment beyond first aid
Loss of consciousness
Diagnosed as a significant injury or illness
1904.7(a)

## Slide 53: Reporting Requirements
Fatalities
  8 hours
Hospitalizations
  24 hours
Amputations
  24 hours
Loss of eye
  24 hours
1904.39

## Slide 54: Respiratory Protection
Focus Areas:

## Slide 55: Respirators
Food manufacturing industry employees can be exposed to a variety of respiratory irritants and hazards.
1910.134
NCDOL Photo Library
NCDOL Photo Library

## Slide 56: Written Program
Written program must contain procedures for:
  Selecting respirators
  Medical evaluations
  Fit testing
  Respirator use
  Respirator maintenance
  Ensuring adequate breathing air for supplied air respirator (SAR)
  Employee training
  Program evaluation
Program must be worksite-specific.
1910.134(c)(1)

## Slide 57: Training and Information
Required:
  Prior to requiring the employee to use a respirator
  Annually
  When changes in workplace render previous training obsolete
  Employee use demonstrates inadequate training
  Any other situation arises in which retraining appears necessary
1910.134(k)(3)-(5)

## Slide 58: Training Topics
1910.134(k)(1)
Why the respirator is necessary and how improper fit, usage, or maintenance can compromise the protective effect of the respirator.
Limitations and capabilities of the respirator.
How to effectively use the respirator in emergencies.

## Slide 59: Training Topics
1910.134(k)(1)
How to inspect, don, doff, use, perform seal checks.
Maintenance and storage procedures.
How to recognize medical signs and symptoms that may limit or prevent the effective use of respirators.
General requirements of the standard.

## Slide 60: When is Fit Testing Required?
Before initial use
Annually, thereafter
When facial features change, such as with weight gain or loss, use of dentures
Note: Employees wearing tight-fitting face-pieces must not be fit tested if they have facial hair. *
1910.134(f)

## Slide 61: Bloodborne Pathogens
Focus Areas:

## Slide 62: Exposure Control Plan
Written plan designed to eliminate or minimize employee exposure that contains:
  Exposure determination
  Schedule and method of implementing paragraphs
  (d) through (h) of the standard
  Procedures for evaluating circumstances surrounding an exposure incident
  Must be reviewed at least annually
1910.1030(c)(1)(ii)

## Slide 63: Potential Occupational Exposure
In food manufacturing potential exposures typically occur through:
  Onsite nurse/medical staff
  Employees required to perform collateral 1st aid duties

## Slide 64: Example Violations
Serious: 1910.1030(c)(2)(i)(A)
  Bloodborne pathogens exposure determination did not include a list of all job classifications in which all employees in those job classifications had occupational exposure.
NC Photo Library

## Slide 65: Process Safety Management
Focus Areas:

## Slide 66: Process Safety Management
1910.119 – Process Safety Management
  Applies to facilities with large refrigeration units or freezer processes.
  Processes which involves chemicals at or above specified Threshold Quantities (TQ), Appendix A.
Main purpose:
  To proactively identify, evaluate, and mitigate or prevent highly hazardous chemical releases.
Requires a written plan of action/program and employee consultation.
1910.119

## Slide 67: List of Hazardous Chemicals Appendix A
Most common products above threshold quantities:
  Anhydrous ammonia (10,000 Ibs. TQ)
  Chlorine (1,500 Ibs. TQ)

## Slide 68: PSM: 14 Elements of Compliance
Employee Participation
Process Safety Information
Process Hazard Analysis
Operating Procedures
Training
Contractors
Pre-Startup Safety Review

## Slide 69: PSM: 14 Elements of Compliance
Mechanical integrity
Hot Work Permit
Management of Change
Incident Investigation
Emergency Planning and Audits
Compliance Audits
Trade Secrets

## Slide 70: Occupational Noise
Focus Areas:

## Slide 71: Occupational Noise
Noise hazards in food manufacturing
  Machinery, processes, and equipment produce high noise levels

## Slide 72
No employee shall be exposed above the permissible exposure level (PEL)
  PEL = 90 decibels on the A scale (dBA) for 8-hour time-weighted average (TWA)
  Action level (AL) – 85 dBA – 8-hour TWA
Feasible engineering and administrative controls are required before personal protective equipment (PPE) can be used.
Permissible Exposure Level
1910.95(b)

## Slide 73: Example Noise Hazard
When employees are exposed to high noise serious/permanent hearing loss can result.
  1910.95(d)(1)
  When information indicates that any employee's exposure may equal or exceed an 8-hour time-weighted average of 85 decibels, the employer shall develop and implement a monitoring program.
1910.95(d)(1)

## Slide 74: Other Hazards
Focus Areas:

## Slide 75: Other Hazards
Personal protective equipment
  1910.132 - Hazard assessment and training
    Involve managers and workers
Example PPE in Food Manufacturing
  Cut resistant gloves/arm guards
  Chemical gloves
  Protective clothing and boots (slip resistant shoes)
29 CFR 1910

## Slide 76: Other Hazards
1910.141 – Sanitation
  Clean water to wash hands
  Adequate number of toilets
  Employees must have access to facilities in timely manner
1910.141

## Slide 77: Other Hazards
Thermal stressors:
  Can be found in various locations in the facility (Live-kill areas, boilers, etc.).
  Engineering/administrative controls in place, PPE assessed.
  Adequate supplies potable/drinkable water must be available for employees in a timely manner.
    Avoid heat stress injuries.

## Slide 78: Other Hazards
Biological/zoonotic disease hazards:
  Medical record/OSHA 300 log evaluations
  Employer’s efforts to control hazards/prevent exposure will be assessed.
Example: Brucellosis
  Bacterium found in infected cattle or swine.
  Workers can contract via inhalation or direct bodily contact with infected blood or tissue.

## Slide 79: Other Hazards
Emergency Action Plan (EAP)
  1910.38 - Essential due to chemicals used in food manufacturing

## Slide 80: Summary
During this course, we covered:
  Food Manufacturing Special Emphasis Program
  Implications for N.C. employers
  Compliance focus areas during an inspection

## Slide 81: Thank You For Attending!
Final Questions?
1-800-NC-LABOR
(1-800-625-2267)
www.labor.nc.gov