## Slide 1: Tools - Hand and Power
29 CFR 1926 Subpart I
Presented by:
Notes: Revised 10/2021
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education, Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
At the end of this course, students will be able to:
  Familiarize themselves with OSHA’s minimum requirements for hand and power tools
  Identify safe design, installation, and use of tools
  Identify various tool hazards and abatement methods
1926 Subpart I

## Slide 3
Goal to reduce occupational exposures to amputations
Struck by and caught between injuries
  Lockout/tagout
  Machine guarding
Increase outreach to employers and employees
  Training events (Internal and external)
  Compliance inspections
  Consultation visits
  Publications
Amputations must be reported within 24 hours
Amputations Special Emphasis Program

## Slide 4: Subpart I: Tools – Hand and Power
1926.300 – General requirements
1926.301 – Hand tools
1926.302 – Power-operated hand tools
1926.303 – Abrasive wheels and tools

## Slide 5: Subpart I: Tools – Hand and Power
1926.304 – Woodworking tools
1926.305 – Jacks: lever and ratchet, screw, and hydraulic
1926.306 – Air receivers
1926.307 – Mechanical power-transmission apparatus

## Slide 6: Common Hand and Power Tools
Hand Tools | Power Tools
Hammers Saws Chisels Shovels Pry bars Pliers Screwdrivers Wrenches Measuring tools | Electric/air/powder Drill motors Nailers/staplers Impact wrenches Impact/roto hammers Jackhammers Soil tampers/compactors Grinders Bandsaws/block saws/table saws Powder actuated tools Concrete mix/vibrators

## Slide 7: Basic Tool Safety Rules
Maintain regularly
Inspect before use
Operate according to manufacturer’s recommendations
Use appropriate PPE
Use guards

## Slide 8: General Requirements
All hand and power tools furnished by the employer, or the employee must be maintained in a safe condition.
1926.300(a)

## Slide 9: Guarding
Belts, gears, shafts, pulleys, sprockets, spindles, drums, fly wheels, chains, or other reciprocating, rotating or moving parts of equipment shall be guarded if such parts are exposed to contact by employees or otherwise create a hazard.
1926.300(b)(2)

## Slide 10: Guarding
NCDOL Photo Library
Guarding provided to protect employees from hazards created by:
  Point of operation
  Ingoing nip points
  Rotating parts
  Flying chips and sparks
1926.300(b)(3)
Non-compliant table saw with guard removed

## Slide 11: Types of Guarding
Fixed guards
Interlocked guards
Adjustable guards
Self-adjusting guards
Fixed Guard
1926.300(b)

## Slide 12: Point of Operation Guarding
Point of operation
  Area on a machine where work is actually performed upon the material being processed.
  Shall be guarded.
Special hand tools for placing and removing material shall be such as to permit easy handling of material without the operator placing a hand in the danger zone.
1926.300(b)(4)

## Slide 13: Miscellaneous Aids
Holding tools
Push stick or block
Awareness barriers
Shields
Push stick does not eliminate blade guard requirement.

## Slide 14: Exposure of Blades
Blades of fans less than 7 feet above floor must be guarded.
Guard openings no larger than ½ inch.
1926.300(b)(5)
Note hazards in this photo: There are several issues (including guard opening).

## Slide 15: Anchoring Fixed Machinery
Machines designed for fixed location must be anchored to prevent walking or moving.
1926.300(b)(6)

## Slide 16: Personal Protective Equipment
Employees exposed to the hazard of falling, flying, abrasive, and splashing objects, or exposed to harmful dusts, fumes, mists, vapors, or gases, shall be provided with the personal protective equipment necessary to protect them from the hazard.
1926.300(c)

## Slide 17: Switches
Positive “on-off” control
  Routers, planers, shears, scroll saws, laminate trimmers, jig saws, nibblers
Momentary contact “on-off”
control
  Power drills, grinders, tappers, disc
  and belt sanders, reciprocating saws
Constant pressure switch
  Circular saw, chain saw, and
  percussion tools
1926.300(d)

## Slide 18: Hand Tool Hazards
Employers shall not issue or permit the use of unsafe hand tools.
Wrenches shall not be used when jaws are sprung to the point that slippage occurs.
Impact tools shall be kept free of mushroomed heads.
Wooden handles shall be kept free of splinters or cracks and shall be kept tight in the tool.
1926.301(a) - (d)
Cracked handle

## Slide 19: Power-Operated Hand Tools
Electric power operated tools shall either be of the approved double-insulated type or grounded in accordance with Subpart K of this part.
Double - insulated markings
Plug with a grounding pin
1926.302(a)(1)

## Slide 20: Power-Operated Hand Tools
Use of electric cords for hoisting or lowering tools shall not be permitted.
1926.302(a)(2)

## Slide 21: Power-Operated Hand Tools
Pneumatic power tools
  Shall be secured to the hose or whip by some positive means to prevent the tool from becoming accidentally disconnected.
1926.302(b)(1)
Positive locking device
Improper and unsecure

## Slide 22: Power-Operated Hand Tools
Pneumatic power tools
  Must have a safety device on the muzzle to prevent the tool from ejecting fasteners unless the muzzle is in contact with work surface.
    Covers tools operating at more than 100 p.s.i.
1926.302(b)(3)
Framing nailer

## Slide 23: Power-Operated Hand Tools
Compressed air must not be used for cleaning.
  Exception
    Where reduced to less than 30 p.s.i. with effective chip guarding and PPE
1926.302(b)(4)

## Slide 24: Power-Operated Hand Tools
Airless spray guns
  Operating at 1,000 p.s.i. or more must be equipped with an automatic or visible manual safety device.
  Safety device prevents pulling trigger until manually released.
1926.302(b)(8)

## Slide 25: Power-Operated Hand Tools
Abrasive blast cleaning nozzles
  Must be equipped with operating valve which must be held open manually.
1926.302(b)(10)
Correct
Incorrect – Valve is held in open position by a hose clamp.

## Slide 26: Power-Operated Hand Tools
Fuel powered tools must be stopped while being refueled, serviced, or maintained.
Fuel must be transported, handled, and stored in accordance with Subpart F- Fire Protection and Prevention.
1926.302(c)(1)
Non-compliant soil tamper
due to missing belt guard.

## Slide 27: Powder-Actuated Tools
User must be trained.
Test tool each day before loading to ensure the safety devices are working properly.
Any tool found not in proper working order, or that develops a defect during use, shall be immediately removed from service.
Wear suitable ear, eye, and face protection.
1926.302(e)

## Slide 28: Powder-Actuated Tools
Don’t use in explosive or flammable atmosphere.
Tools shall not be loaded until just prior to intended firing time.
1926.302(e)

## Slide 29: Powder-Actuated Tools
Keep hands clear of the barrel end.
Never point the tool at anyone.
Use with the correct shield, guard, or attachment recommended by the manufacturer.
Loaded tools shall not be left unattended.
1926.302(e)

## Slide 30: A Fatal Fact
A 22-year-old carpenter’s apprentice was killed when struck in head by a nail fired from a powder actuated tool.
Tool operator was attempting to anchor a plywood form in preparation for pouring a concrete wall.
Tool operator had never received training on how to properly use the tool.
All area employees were not wearing PPE.

## Slide 31: Abrasive Wheel Machinery
Distance between the wheel periphery and the adjustable tongue shall not exceed ¼ inch.
1926.300(b)(7)
Tongue guard out of adjustment

## Slide 32: Abrasive Wheels and Tools
Abrasive wheels shall be used only on machines provided with safety guards.
Wheel safety guards cover the spindle end, nut, and flange projections.
1926.303(b)(1)-(2)
NCDOL Photo Library

## Slide 33: Use of Abrasive Wheels
NCDOL Photo Library
270-degree guard
Floor and bench-mounted grinders
  Angular exposure of the grinding wheel periphery and sides for safety guards used on machines should not exceed 90 degrees or
  ¼ of the periphery.
1926.303(c)(1)

## Slide 34: Use of Abrasive Wheels
Work rests must be adjusted closely to the wheel with a maximum opening of ⅛ inch.
1926.303(c)(2)

## Slide 35: Use of Abrasive Wheels
Vertical portable grinders must have safety guard on tool with a maximum exposure angle of 180 degrees.
1926.303(c)(5)
Non-compliant portable grinders without guards.

## Slide 36: Use of Abrasive Wheels
Install the proper type guard located so as to be between the operator and the wheel during use.
Guard adjusted to deflect broken pieces of wheel away from operator.
1926.303(c)(5)

## Slide 37: Use of Abrasive Wheels
All abrasive wheels must be closely inspected and ring-tested before mounting to ensure that they are free from cracks and defects.
1926.303(c)(7)
NCDOL Photo Library

## Slide 38: Use of Abrasive Wheels
Ensure the spindle speed does not exceed the maximum speed marked on the wheel.
Grinding wheels must fit freely on the spindle.
Tighten the spindle nut only enough to hold the wheel in place.
1926.303(c)(8)
Maximum RPM 8,700

## Slide 39: Woodworking Tools
Fixed power-driven woodworking tools must be provided with a disconnect switch.
Switch can either be locked or tagged in
the off position.
1926.304(a)

## Slide 40: Woodworking Tools
Portable circular saws
  Must be equipped with guards above and below the base plate or shoe.
  Upper and lower guard must cover the saw to the depth of the teeth.
  Lower guard must automatically return to the covering position over the blade teeth when tool is withdrawn from the work.
  Mechanical or electrical power control provided for operator to cut off power.
    Control is located on machine where operator does not have to leave his position at the point of operation.
1926.304(d), (f)

## Slide 41: Woodworking Tools
Jointers
  Hand-fed jointer with horizontal cutting head must have an automatic guard.
    Must cover the working side of the fence or gage
    Automatically adjust and cover the unused portion of the head
1926.304(f)

## Slide 42: Woodworking Tools
Hand-fed jointers
  With horizontal cutting head must have a guard.
  Must cover the section of head back of the gage or fence.
1926.304(f)

## Slide 43: Woodworking Tools
Bandsaws and band re-saws
  All portions of saw blade must be enclosed or guarded except working portion between guide rollers and the table.
  Bandsaw wheels must be fully encased.
1926.304(f)
NCDOL Photo Library

## Slide 44: Woodworking Tools
Radial saws
  Guard to prevent the operator from coming in contact with the rotating blade.
1926.304(g)(1)
NCDOL Photo Library

## Slide 45: Woodworking Tools
Radial saws
  Lower portion of blade must be guarded on both sides.
    Guarded to the full diameter of the blade
    Will adjust itself to
    the thickness of the
    stock
NCDOL Photo Library
This saw does not comply
with the requirement.
1926.304(g)(1)

## Slide 46: Woodworking Tools
Hand-fed ripsaws
  Provided with a hood guard.
  Hood must completely enclose portion of saw blade above the table.
  Mounting must be strong enough to resist any reasonable side thrust.
Spreader
1926.304(i)(1)

## Slide 47: Woodworking Tools
Hand-fed ripsaws
  Hood guard must automatically adjust itself to thickness of material being cut.
  Remain in contact with material.
1926.304(i)(1)

## Slide 48: Jacks
Manufacturer’s rated capacity must be marked on all jacks and must not be exceeded.
All jacks must have a positive stop to prevent over travel.
1926.305(a)(1)

## Slide 49: Jacks
Operation
  Base seated on a firm, level surface
  Where there is a possibility of slippage
    Use wood block between cap and load
    Crib, block, or secure
    load after it is raised
1926.305(c), (d)(1)(i)

## Slide 50: Jacks
Maintenance
  Properly lubricate and inspect at regular intervals.
  Repair or replacement parts shall be examined for possible defects.
  Defective jacks removed from service until repaired.
1926.305(d)(1)(iii)-(vi)

## Slide 51: Air Receivers
Air receiver must be constructed in accordance with American Society of Mechanical Engineers (ASME) Boiler and Pressure Code Section VIII – 1968.
1926.306(a)(2)
Notes: .

## Slide 52: Air Receivers
Installed so that all drains, handholds, and manholes are easily accessible.
1926.306(b)(1)

## Slide 53: Air Receivers
Must be equipped with an indicating pressure gage and at least one spring-loaded safety valve.
Safety valves must be tested frequently and at regular intervals to determine operating condition.
1926.306(b)(3)(i)-(iv)

## Slide 54: Mechanical Power–Transmission Apparatus
Exposed parts of horizontal shafting 7 feet or less from floor or working platform must be guarded.
1926.307(c)(2)(i)

## Slide 55: Mechanical Power–Transmission Apparatus
Must not project more than ½ the diameter of the shaft or unless guarded by nonrotating caps or safety sleeves.
1926.307(c)(4)(i)

## Slide 56: Mechanical Power–Transmission Apparatus
Any parts of pulleys which are 7 feet or less from floor or working platform shall be guarded.
1926.307(d)(1)

## Slide 57: Mechanical Power–Transmission Apparatus
Where both runs of horizontal belts are 7 feet or less from floor level,
  Guard must extend at least 15 inches above the belt.
Horizontal belt with both runs 42 inches or less from floor must be fully enclosed.
1926.307(e)(1)(i)

## Slide 58: Mechanical Power–Transmission Apparatus
Vertical and inclined belts less than 7 feet above floor or platform must be guarded.
1926.307(e)(3)

## Slide 59: Mechanical Power–Transmission Apparatus
All sprocket wheels and chains shall be enclosed unless more than 7 feet above floor or platform.
1926.307(f)(3)

## Slide 60: Summary
In this course, we discussed:
  OSHA’s minimum requirements for hand and power tools
  Safe design, installation, and use of tools
  Hazard identification
  Abatement methods

## Slide 61: Thank You For Attending!
Final Questions?