## Slide 1: Control of Hazardous Energy (Lockout/Tagout)
29 CFR 1910.147
Notes: Revised 06/2025
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education, Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.
NCDOL References:
HAZARDOUS ENERGY CONTROL (Lockout/Tagout)
CPL 02-00-147 Control of Hazardous Energy
CPL 02-01-043 Slide-locks-Control of Hazardous Energy
CFR 106 Lockout/Tagout
CFR 106A Lockout/Tagout

## Slide 2: Objectives
After this course, students will be able to:
  Understand the need for energy control procedures
  Identify methods of lockout/tagout
  Identify the employer’s responsibilities
  Identify the employee training needs
  Understand how to handle group lockout/tagout, outside contractors, and shift changes

## Slide 3
Goal to reduce occupational exposures to amputations
Struck by and caught between injuries
  Lockout/tagout
  Machine guarding
Increase outreach to employers and employees
  Training events (Internal and external)
  Compliance Inspections
  Consultation Visits
  Publications
Amputations must be reported within 24 hours
Amputations Special Emphasis Program

## Slide 4: Lockout/Tagout
Technically known as the “Control of Hazardous Energy”
  Control of unexpected energization or start-up of machines or equipment, or release of stored energy that could cause injury to employees
1910.147

## Slide 5: Scope
Covers the servicing and/or maintenance of machines or equipment where the unexpected start-up or release of stored energy could cause injury
  Installation and set-up
  Adjustment or maintenance
  Inspection
  Modification
  Routine service
1910.147(a)(1)

## Slide 6: Scope
Does not cover
  Construction, agriculture, maritime
  Installations under exclusive control of the electric utilities for power generation, transmission and distribution
  Exposure to electrical hazards from work on, near, or with conductors or equipment in electric-utilization installations
  Oil and gas drilling and servicing
1910.147(a)(1)

## Slide 7: Application
Servicing and/or maintenance which takes place during normal production operations is covered only if:
  Employee is required to remove or bypass a guard or other safety device; or
  Employee is required to place any part of his/her body into the point of operation or where an associated danger zone exists during a machine operation.
1910.147(a)(2)

## Slide 8: Application
Exception
  Minor tool changes and adjustments, and other minor servicing activities, which take place during normal production operations, are not covered if they are:
    Routine,
    Repetitive, and
    Integral to the use of the equipment for production
    provided that the work is performed using alternative measures which provide effective protection
1910.147(a)(2)

## Slide 9: Application
Does not cover:
  Normal production operations
  Work on cord and plug connected equipment where plug is under exclusive control of employee performing servicing/maintenance
  Hot tap operations, under special conditions
1910.147(a)(2)

## Slide 10: Definitions
Authorized employee
  An employee who locks out or tags out machines or equipment to perform servicing or maintenance on that machine or equipment
  Lockout or tagout is used by these employees for their own protection
1910.147(b)

## Slide 11: Definitions
Affected employee
  An employee who performs the duties of his or her job on equipment or in an area in which the energy control procedure is implemented and servicing or maintenance operations are performed
1910.147(b)

## Slide 12: Other Employees
Other employees
  Other employees whose work operations are, or may be, in an area where energy control procedures may be utilized
1910.147(c)(7)

## Slide 13
Energy source
  Mechanical
  Hydraulic
  Chemical
  Pneumatic
  Electrical
  Thermal
Definitions
1910.147(b)

## Slide 14: Energy Control Program
The employer shall establish a program consisting of:
  Energy control procedures
  Employee training
  Periodic inspections
1910.147(c)(1)

## Slide 15: Energy Control Program
If an energy isolating device is not capable of being locked out, the employer’s energy control program shall utilize a “tagout system”.
1910.147(c)(2)

## Slide 16: Energy Control Program
When a tagout device is used on an energy isolating device which is capable of being locked out
  Tagout device shall be attached at the same location
  Must provide equivalent safety
1910.147(c)(3)

## Slide 17: Energy Control Procedure
Procedures
  Shall be developed, documented and utilized for the control of potentially hazardous energy
  Shall clearly and specifically outline techniques to be utilized to control hazardous energy
1910.147(c)(4)

## Slide 18: Energy Control Procedure
Energy control (LOTO) procedure
  Statement of intended use of procedure
  Steps for shutting down, isolating, blocking and securing machines or equipment to control hazardous energy
  Steps for the placement, removal and transfer of lockout devices or tagout devices and the responsibility for them, and
  Requirements for testing machine/equipment to determine and verify effectiveness of LOTO devices and other energy control measures
1910.147(c)(4)

## Slide 19: Procedure Exception
    Machine/equipment has no potential for stored/residual energy after shut down
    Machine/equipment has a single energy source (readily identified and isolated
    The isolation and locking out of energy source will completely de-energize/deactivate the machine/equipment
    Machine/equipment is isolated from that energy source and locked out during servicing or maintenance
1910.147(c)(4)

## Slide 20: Procedure Exception
    Lockout device is under the exclusive control of the authorized employee performing the servicing or maintenance
    Servicing/maintenance does not create hazards for other employees; and
    Employer has had no accidents involving the unexpected activation/re-energization of the machine/equipment during servicing/maintenance
1910.147(c)(4)

## Slide 21: Materials and Hardware
Provided by employer
Singularly identified
Only device(s) used
Not used for other purposes
1910.147(c)(5)

## Slide 22: Materials and Hardware
Durable
Standardized
Substantial
Identifiable
1910.147(c)(5)

## Slide 23: Types of Devices

## Slide 24
Is this lockout identifiable?
Based on the photo, it is not.
1910.147(c)(5)

## Slide 25: Periodic Inspection
Conducted at least annually to ensure procedure and requirements are followed
Performed by authorized employee other than the one(s) using the procedure
Designed to correct identified deficiencies or inadequacies
Employer shall certify that periodic inspection has been performed
1910.147(c)(6)

## Slide 26: Periodic Inspection
Lockout inspection
  Must review each authorized employee’s responsibilities under the energy control procedure
Tagout inspection
  Must review each authorized and affected employee’s responsibilities under the energy control procedure, and
  Additional training requirements of 1910.147(c)(7)(ii)
1910.147(c)(6)

## Slide 27: Training and Communication
Authorized employee
  Recognition of hazardous energy sources
  Type and magnitude of energy in workplace
  Methods and means for energy isolation and control
Affected employee
  Purpose and use of the energy control procedure
1910.147(c)(7)

## Slide 28: Training and Communication
All other employees
  Procedures for energy control
  Prohibition of restarting or reenergizing machines that are locked or tagged out
1910.147(c)(7)

## Slide 29: Training and Communication
Tagout system limitations
  Warning devices only; do not provide physical restraint
  Must not be removed/bypassed/ignored
  Must be legible and understandable
  Must withstand environmental conditions
  May evoke false sense of security
  Must be securely attached
1910.147(c)(7)

## Slide 30: Training and Communication
Retraining for authorized and affected employees
  Change in job assignments
  Change in machines, equipment or processes that present new hazards
  Change in energy control procedures
  Whenever periodic inspections reveal, or employer has reason to believe, there are deviations in employee knowledge or use of procedures
1910.147(c)(7)

## Slide 31: Is this a proper lockout?
NO
Why?

## Slide 32: Energy Isolation
Lockout or tagout shall be performed only by the authorized employees who are performing the servicing or maintenance
1910.147(c)(8)

## Slide 33: Notification of Employees
Affected employees shall be notified by the employer or authorized employee of the application and removal of LOTO devices
Notification given before controls are applied, and after they are removed from the machine or equipment
1910.147(c)(9)

## Slide 34: Application of Control
Application of control
  Preparation for shutdown
  Machine or equipment shutdown
  Machine or equipment isolation
  LOTO device application
  Release of stored energy
  Verification of isolation
1910.147(d)

## Slide 35: Preparation for Shutdown
Know the types and amounts of energy
Know the hazards of the energy
Know method or means to control energy
1910.147(d)(1)

## Slide 36: Machine/Equipment Shutdown
Turn off or shut down using established procedures
Utilize orderly shutdown to avoid additional or increased hazard(s) to employees as a result of the equipment stoppage
1910.147(d)(2)

## Slide 37: Machine/Equipment Isolation
All energy isolating devices needed to control energy shall be physically located to isolate the machine or equipment from the energy source(s)
1910.147(d)(3)

## Slide 38: Lockout/Tagout Application
Devices shall be affixed to each energy isolating device by authorized employees
Lockout devices shall be affixed in a manner that will hold the energy isolating devices in a “safe” or “off” position
Tagout devices shall be affixed in a manner indicating that the operation or movement of energy isolating devices from the “safe” or “off” position is prohibited
1910.147(d)(4)

## Slide 39: Release of Stored Energy
After application of device, all potentially hazardous stored or residual energy shall be relieved, disconnected, restrained, and otherwise rendered safe
1910.147(d)(5)

## Slide 40: Verification of Isolation
Prior to starting work on machines or equipment that have been locked out/tagged out
  Authorized employee shall verify that isolation and de-energization of the machine or equipment have been accomplished
1910.147(d)(6)

## Slide 41: Release from Control
Release from LOTO
  Inspection of machine or equipment work area
  Location of employees
  LOTO device removal
1910.147(e)

## Slide 42: Inspection of Work Area
Before LOTO devices are removed and energy restored
  Work area inspected to ensure that nonessential items have been removed and to ensure that machine or equipment components are operationally intact
  Work area shall be checked to ensure that all employees have been safely positioned or removed
  Affected employees notified that LOTO devices are removed
1910.147(e)

## Slide 43: LOTO Device Removal
Each LOTO device shall be removed from each energy isolating device by the employee who applied the device
  Exception: When authorized employee who applied the LOTO device is not available, device may be removed under the direction of the employer
1910.147(e)(3)

## Slide 44: LOTO Device Removal
Employer removal of LOTO device
  Specific procedure shall include:
    Verification by employer that authorized employee who applied device is not at the facility
    Making all reasonable efforts to contact authorized employee to inform them that LOTO device has been removed, and
    Ensuring that authorized employee has this knowledge before they resume work at facility
1910.147(e)(3)

## Slide 45: Testing/Positioning Machines
When LOTO devices must temporarily be removed for testing/positioning:
  Clear machine or equipment of tools and materials
  Remove employees from area
  Remove lockout/tagout device
  Energize and proceed with testing or positioning
  Deenergize and reapply energy control measures
1910.147(f)

## Slide 46: Outside Personnel
Contractors and the on-site employer must exchange lockout/tagout information
On-site employees must understand and comply with rules used by the contractor
1910.147(f)(2)

## Slide 47: Group Lockout/Tagout
When servicing and/or maintenance is performed by a group, they shall utilize a procedure which affords employee protection equivalent to a personal LOTO device
1910.147(f)(3)

## Slide 48: Group Lockout/Tagout
Primary responsibility is vested in an authorized employee
Authorized employee must ascertain exposure status of group members
If more than one crew is involved, a coordinator shall be designated
Each authorized employee shall use a personal LOTO device and remove device when they stop working on machine/equipment
1910.147(f)(3)

## Slide 49: Shift/Personnel Changes
Specific procedures used during shift/personnel changes to ensure the continuity of LOTO protection
  To minimize exposures from the unexpected energization or start-up of the machine/ equipment, or release of stored energy
1910.147(f)(4)

## Slide 50: Sample LOTO Program
Typical minimal lockout procedures
  A non-mandatory guideline to assist employers and employees in complying with the requirements of this section
Appendix A

## Slide 51: Summary
In this course, we covered:
  The need for energy control procedures
  Methods of lockout/tagout procedures
  Employer’s responsibilities
  Employee training needs
  Inspection requirements

## Slide 52: Thank You For Attending!
Final Questions?