## Slide 1: Machinery and Machine Guarding
29 CFR 1910.211–219
29 CFR 1910.241–244
Presented by:
Notes: Revised 06/25
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education, Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.
NCDOL References: MACHINERY AND MACHINE GUARDING
CPL 02-01-025 Power Press Brakes, SN 56A Heavy and Light Duty Pneumatic Staplers
STD 1-12.1 Guarding of Fan Blades, STD 1-12.4 Radial Saws - Labeling
STD 1-12.5 Circular Meat Cutting Saws, STD 1-12.6 Forging Machines
STD 1-12.7 Platen Presses, STD 1-12.10 Machine Guarding –Food Waste Disposal Equipment
STD 1-12.14 Power Transmission Belts, STD 1-12.15 Automatic Cut-off Saws - Guards
STD 1-12.17 Radial Saws – Guards, STD 1-12.18 Ripsaws, Cutoff Saws, & Radial Saws
STD 1-12.19 Sewing Machines – Guards, STD 1-12.22 Engraving Presses – Guards
STD 1-12.23A Three-Roller Printing Ink Mills – Guards, STD 1-12.25A Metal Cutting Shears – Awareness Barriers
STD 1-12.26A Cutoff Wheels and Masonry Saws, STD 1-12.27 Mechanical Power Presses and Iron Workers
STD 1-13.4 Portable Belt Sanders – Guards, CFR 170 Mechanical Power Transmission Apparatus

## Slide 2: Objectives
After this course, students will be able to:
  Identify machine guarding hazards
  Understand machine guarding abatement methods
  Become familiar with the machine guarding standards

## Slide 3: Machinery and Machine Guarding
1910.211 – Definitions
1910.212 – General requirements for all machines
1910.213 – Woodworking machinery requirements
1910.215 – Abrasive wheel machinery
1910.217 – Mechanical power presses
1910.219 – Mechanical power-transmission apparatus

## Slide 4: Hand and Portable Powered Tools
1910.241 – Definitions
1910.242 – Hand and portable powered tools and equipment, general
1910.243 – Guarding of portable powered tools
1910.244 – Other portable tools and equipment

## Slide 5
Goal to reduce occupational exposures to amputations
Struck by and caught between injuries
  Lockout/tagout
  Machine guarding
Increase outreach to employers and employees
  Training events (Internal and external)
  Compliance inspections
  Consultation visits
  Publications
Amputations must be reported within 24 hours
Amputations Special Emphasis Program

## Slide 6: Mechanical Hazards
MOTIONS | ACTIONS
Rotating | Cutting
In-running nip points | Punching
Reciprocating | Shearing
Transverse | Bending
Notes: 6

## Slide 7: Methods of Guarding
Guards
Devices
Location/distance
Feed mechanisms
Miscellaneous aids

## Slide 8: Machine Guards
Guards are barriers that prevent access to danger areas
  Fixed guards
  Interlocks
  Adjustable
  Self-adjusting

## Slide 9: Machine Guarding 1910.212(a)(1)
Guarding provided to protect employees from hazards created by:
  Point of operation
  Ingoing nip points
  Rotating parts
  Flying chips and sparks

## Slide 10: Machine Guarding 1910.212(a)(1)
Barrier guards

## Slide 11: Machine Guarding 1910.212(a)(1)
Adjustable guard

## Slide 12: Safeguarding Devices
Photoelectric presence-sensing
Radiofrequency
Electromechanical sensing device
Pullbacks
Restraints
Safety trip controls
Two-hand controls
Two-hand trip
Gates
Two Hand Control
NCDOL Photo Library

## Slide 13: Machine Guarding 1910.212(a)(1)
Presence-sensing device

## Slide 14: Machine Guarding 1910.212(a)(1)
Pull-out device

## Slide 15: Machine Guarding 1910.212(a)(1)
A holdout or restraint device

## Slide 16: Machine Guarding 1910.212(a)(1)
Two-hand tripping devices

## Slide 17: Location/Distance
Hazard analysis
Hazards are not accessible
Walls
Fences
Height
Stock dimension
Operator’s station

## Slide 18: Feed Mechanisms
Automatic feeding
Semi-automatic feed
Automatic ejection
Semi-automatic ejection
Robots

## Slide 19: Miscellaneous Aids
Awareness barriers
Shields
Holding tools
Push stick or block

## Slide 20: Safeguard Requirements
Prevent contact
Properly secured
Protect from falling objects
Create no hazards
Create no interference (greater hazard)
Allow safe lubrication (removal of guards)

## Slide 21: General Requirements 1910.212(a)(2)
Guards affixed to machine where possible
  Guard must not offer an accident hazard in itself

## Slide 22: General Requirements 1910.212(a)(3)
Machine guarding for all machines
  Point of operation of
  machines whose operation
  exposes an employee to injury,
  shall be guarded
  Special hand tools for placing
  and removing material must
  permit easy handling of material
    Without the operator placing a hand in
    the danger zone

## Slide 23: General Requirements 1910.212(a)(5)
Exposure of blades
  Blades of fans less than 7 feet above floor or working level must be guarded
  Guard openings must be no larger than ½ inch
vs.

## Slide 24: Fan Blades Not Properly Guarded
Corrective action
  Install proper guard over fan blades with opening no larger than ½ inch

## Slide 25: General Requirements 1910.212(b)
Anchoring fixed machinery
  Machines designed for fixed location must be anchored to prevent walking or moving

## Slide 26: Woodworking Machinery 1910.213(b)(1)
Machine controls and equipment
  Mechanical or electrical power control provided for operator to cut off power
  Located on machine
  where operator does
  not have to leave his
  position at the point
  of operation

## Slide 27: Woodworking Machinery 1910.213(b)(3)
Machine controls and equipment
  Provision to prevent machines from automatically restarting upon restoration of power

## Slide 28: Woodworking Machinery 1910.213(c)(1)-(c)(3)
Hand-fed ripsaw
  Provided with a hood guard
  Provided with a spreader
  Provided with non-kickback fingers or dogs

## Slide 29: Woodworking Machinery 1910.213(c)(1)
Hand-fed ripsaw
  Hood guard must automatically adjust itself to thickness of material being cut
    Remain in contact
    with material
USDOL Photo Library

## Slide 30: Woodworking Machinery 1910.213(h)(1)
Radial saws
  Upper hood must completely enclose upper portion of blade
    Must include the end of
    the saw arbor

## Slide 31: Woodworking Machinery 1910.213(h)(1)
Radial saws
  Lower portion of blade must be guarded on both sides
    Guarded to the full diameter of the blade
    Will adjust itself to the thickness of the stock

## Slide 32: Woodworking Machinery 1910.213(h)(1)

## Slide 33: Woodworking Machinery 1910.213(h)(2)–(h)(5)
Radial saws
  Saw used for ripping provided with non-kickback fingers or dogs
  Ripping must be against the direction which the saw turns
  Adjustable stops preventing forward travel of blade beyond position necessary to complete cut
  Cutting head must return to starting position when released

## Slide 34: Woodworking Machinery 1910.213(i)(1)
Bandsaws and band re-saws
  All portions of saw blade must be enclosed or guarded
    Except working portion between guide rollers and the table
NCDOL Photo Library

## Slide 35: Woodworking Machinery 1910.213(j)(3)-(j)(4)
Jointers
  Hand-fed jointers with horizontal cutting heads must have an automatic guard that covers the working side of the fence or gage and automatically adjusts and covers the unused portion of the head
  Hand-fed jointers with horizontal cutting heads must also have a guard that covers the section of head back of the gage or fence

## Slide 36: Woodworking Machinery 1910.213(p)(3)
Disk sanding machine
  Exhaust hood or guard arranged to enclose revolving disk
    Except portion above table

## Slide 37: Woodworking Machinery 1910.213(p)(4)
Belt sanding machines
  Guards provided at each nip point where sanding belt runs on to a pulley

## Slide 38: Abrasive Wheel Machinery 1910.215(a)(4)
Work rests must be adjusted closely to the wheel with a maximum opening of ⅛ inch

## Slide 39: Abrasive Wheel Machinery 1910.215(a)(4)
Work rests must be adjusted closely to the wheel with a maximum opening of ⅛ inch

## Slide 40: Abrasive Wheel Machinery 1910.215(b)(9)
Distance between the wheel periphery and the adjustable tongue must not exceed ¼ inch
NCDOL Photo Library

## Slide 41: Abrasive Wheel Machinery 1910.215(b)(9)
Corrective action
  Properly adjust the work rest and tongue guard to allowable openings

## Slide 42: Abrasive Wheel Machinery 1910.215(b)(3)
Bench and floor stands
  The angular exposure of the grinding wheel periphery and sides for safety guards used on machines should not exceed 90 degrees or ¼ of the periphery
NCDOL Photo Library
NCDOL Photo Library

## Slide 43: Abrasive Wheel Machinery 1910.215(d)(1)
Inspection
  All abrasive wheels must be closely inspected and ring-tested before mounting to ensure that they are free from cracks and defects
NCDOL Photo Library

## Slide 44: Mechanical Power Presses 1910.217(b)(4)(i)
Foot pedals (treadle)
  Pedal mechanism shall be protected to prevent unintended operation
    From falling or moving
    objects
    Accidental stepping
    onto the pedal

## Slide 45: Mechanical Power Presses
Safeguarding the point of operation
  Point of operation must be provided with guards or point of operation devices
Presence sensing point of operation device
  Must be interlocked into the control circuit to
  prevent or stop slide motion if part of operator’s body is within sensing field during down stroke of press slide
Presence sensing point of operation device
  Presence sensing devices cannot be used on machines using full revolution clutches
1910.217(c)(1), (c)(3)(iii)(a)

## Slide 46: Mechanical Power Presses 1910.217(c)(3)(iv)
Pull-out device shall include attachments for each of operator’s hands
  Connected to and operated only by press slide of upper die
  Visually inspected and properly adjusted at start of each operator shift
  Properly adjusted

## Slide 47: Mechanical Power-Transmission Apparatus
Prime-mover guards
  Flywheels with any part 7 feet or less above floor or platform must be guarded
  1910.219(b)(1)

## Slide 48: Mechanical Power-Transmission Apparatus
Shafting
  Exposed parts of horizontal shafting 7 feet or less from floor or working platform must be guarded
  1910.219(c)(2)(i)

## Slide 49: Mechanical Power-Transmission Apparatus
Projecting shaft ends
  Must not project more than ½ the diameter of the shaft
    Unless guarded by non-rotating caps or safety sleeves
NCDOL Photo Library
  1910.219(c)(4)(i)

## Slide 50: Mechanical Power-Transmission Apparatus
Pulleys
  Any parts of pulleys which are 7 feet or less from floor or working platform must be guarded
  1910.219(d)(1)

## Slide 51: Mechanical Power-Transmission Apparatus
Where both runs of horizontal belts are 7 feet or less from floor level
  Guard must extend at least 15 inches above
  the belt
Horizontal belt with both runs 42 inches or less from floor must be fully enclosed
NCDOL Photo Library
  1910.219(e)(1)(i)

## Slide 52: Mechanical Power-Transmission Apparatus
Vertical and inclined belts must be enclosed
by a guard
  1910.219(e)(3)(i)

## Slide 53: Mechanical Power-Transmission Apparatus
Gears must be guarded by complete enclosures or standard guard
  1910.219(f)(1)

## Slide 54: Mechanical Power-Transmission Apparatus
Sprockets and chains
  Sprocket wheels and chains located 7 feet or less above the floor or platform must be enclosed
  1910.219(f)(3)

## Slide 55: Mechanical Power-Transmission Apparatus
Keys, setscrews, and other projections
  Projecting keys, setscrews, and other projections in revolving parts must be removed, made flush, or guarded
  1910.219(h)(1)

## Slide 56: Mechanical Power-Transmission Apparatus
Shaft couplings must be constructed as to present no hazard from bolts, nuts, setscrews, or revolving surfaces
  Permitted where they are
  covered with safety sleeves
  or countersunk and do not
  extend beyond the flange
  of the coupling
  1910.219(i)(2)

## Slide 57: Portable Powered Tools 1910.243(a)(1)(i)
Portable circular saws
  Must be equipped with guards above and below the base plate or shoe
  Lower guard must cover the saw to the depth of the teeth

## Slide 58: Portable Powered Tools 1910.243(a)(1)(i)
Portable circular saws
  Lower guard must automatically return to the covering position over the blade teeth
    When tool is withdrawn from the work
NCDOL Photo Library

## Slide 59: Portable Powered Tools 1910.243(a)(2)(i)
Switches and controls
  All hand-held powered circular saws must be equipped with a constant pressure switch or control
    Will shut off the power when the pressure is released

## Slide 60: Portable Powered Tools 1910.243(a)(2)(ii)
Electric tools must be equipped with switches that must be equipped with a constant pressure switch, or
Turnoff can be accomplished by a single motion of same finger or fingers that turn it on
NCDOL Photo Library

## Slide 61: Portable Powered Tools 1910.243(a)(3)
Portable belt sanding machines
  Must have guards at nip points where belt runs onto a pulley
  Unused portion of the belt must be guarded

## Slide 62: Portable Powered Tools 1910.243(b)(2)
Pneumatic powered tools and hose
  Hose and hose connections shall be designed for pressure and service which they are subjected
Proper Tool Connection
Improper Hose Connection

## Slide 63: Portable Powered Tools 1910.243(c)(3)
Vertical portable grinders
  Must have safety guard on tool with a maximum exposure angle of 180 degrees

## Slide 64: Portable Powered Tools 1910.243(c)(3)
Corrective action
  Install proper type of guard
    Guard must be located so as to be between the operator and the wheel during use

## Slide 65: Summary
In this course, we covered:
  Machine guarding hazards
  Machine guarding abatement methods
  Machine guarding standards

## Slide 66: Thank You For Attending!
Final Questions?