## Slide 1: Personal Protective Equipment Construction Industry – Subpart E
29 CFR 1926.95 - 1926.106
Notes: Revised 6/16/25
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
After this course, students will:
Understand general provisions of the standard
Recognize basic hazard categories
Be able to identify hazard sources and personal protective equipment (PPE)
NCDOL Photo Library

## Slide 3: What is PPE?
Equipment that creates a barrier against workplace hazards
Examples include hard hats, goggles, gloves and hearing protection
A temporary measure
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library

## Slide 4: General Requirements
Personal protective equipment
  Establish and supervise programs for the education and training of employers and employees in the recognition, avoidance and prevention of unsafe conditions in employments covered by the act
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library
No fall protection used

## Slide 5: General Safety and Health Provisions
Personal protective equipment
1926.28(a)
NCDOL Photo Library
  Employer is responsible for requiring the wearing of appropriate PPE in all operations where there is an exposure to hazardous conditions
NCDOL Photo Library

## Slide 6: General Safety and Health Provisions
Personal protective equipment
  Employees required to handle or use poisons, caustics, and other harmful substances shall be instructed regarding the safe handling and use, and be made aware of the potential hazards, personal hygiene, and personal protective measures required
NCDOL Photo Library
NCDOL Photo Library
1926.21(b)(3)
NCDOL Photo Library

## Slide 7: Training
Employer shall instruct each employee in the recognition and avoidance of unsafe conditions and the regulations applicable to his work environment to control or eliminate any hazards or other exposure to illness or injury
1926.21(a)-(b)
NCDOL Photo Library

## Slide 8: Criteria for PPE
Protective equipment, including PPE for eyes, face, head, and extremities shall be provided, used, and maintained in a sanitary and reliable condition
1926.95(a)
NCDOL Photo Library
NCDOL Photo Library
LOI Masons
Not PPE !
No PPE !

## Slide 9: Criteria for PPE
Employee-owned equipment
  Where employees provide their own protective equipment, the employer shall be responsible to assure its adequacy, including proper maintenance, and sanitation of such equipment
1926.95(b)
NCDOL Photo Library
NCDOL Photo Library

## Slide 10: Criteria for PPE
Design
  All personal protective equipment shall be of safe design and construction for work to be performed
1926.95(c)
NCDOL Photo Library
NCDOL Photo Library
Not correct

## Slide 11: Payment for PPE
Except as noted, the protective equipment used to comply with this part shall be provided by the employer at no cost to employees
Exception:
  Everyday clothing, such as long-sleeve shirts, long pants, street shoes, and normal work boots
1926.95(d)(2)-(5)
NC DOL Photo Library

## Slide 12: Training Documentation
Employers should prepare a record which contains the identity of the employee, the date of training, and the means used to verify that the employee understood the training
  Some construction standards require documentation/ certification of PPE training including:
    HAZWOPER (1926.65)
    Fall Protection (1926.503)
    Confined Spaces in Construction (1926.1207)
    Many Health Standards (Subpart D, Subpart Z)

## Slide 13: Basic Hazard Categories
Impact
Penetration
Compression
Chemical
Electrical shock
Electrical arc
Harmful dust
Light radiation
Falls
Heat

## Slide 14: Hazard Sources
Motion
Temperature
Chemical exposure
Light radiation
Elevation
Sharp objects
Rolling/pinching
Electrical hazards
Workplace layout
Worker location
NCDOL Photo Library
NCDOL Photo Library

## Slide 15: Electrical Protection
NCDOL Photo Library
Electrical protective equipment shall be maintained in a safe, reliable condition
  Rubber insulating blankets, matting, covers, line hose, gloves, and sleeves
1926.97
Rating of gloves - Stamped - Class Protection “0”
LOI Head Protection
NCDOL Photo Library

## Slide 16: Electrical Protection
NCDOL Photo Library
Design requirements for specific types of electrical protective equipment
1926.97(c)(1)
Glove and arm protection
NCDOL Photo Library
LOI Head Protection
  Electrical protective equipment shall be maintained in a safe, reliable condition
  Must conform to those listed in Table E-4

## Slide 17: Head Protection
Employees working in areas where there is a possible danger of head injury from impact, or from falling or flying objects, or from electrical shock and burns, shall be protected by helmets
1926.100(a)
Built-in eye protection
NCDOL Photo Library
LOI Head Protection

## Slide 18: Head Protection
Helmets for protection of employees against impact and penetration of falling and flying objects shall meet specification in any of the following consensus standards:
1926.100(b)
NCDOL Photo Library
  American National Standards Institute (ANSI) Z89.1-2009
  ANSI Z89.1-2003
  ANSI Z89.1-1997

## Slide 19: Hearing Protection
Wherever it is not feasible to reduce noise levels or duration of exposure to those specified in 29 CFR 1926.52, Table D-2, Permissible Noise Exposures, ear protection devices shall be provided and used
1926.101(a)
NCDOL Photo Library
NCDOL Photo Library

## Slide 20: Hearing Protection
Ear protection devices inserted in the ear shall be fitted or determined individually by a competent person
Plain cotton is not an acceptable protective device
1926.101(b)-(c)
NCDOL Photo Library
No eye, ear or face protection
NCDOL Photo Library

## Slide 21: Eye and Face Protection
Employees shall be provided with eye and face protection equipment when machines or operations present potential eye or face injury from physical, chemical, or radiation agents
1926.102(a)(1)
NCDOL Photo Library
NCDOL Photo Library

## Slide 22: Eye and Face Protection
Eye and face protection equipment must meet:
  ANSI Z87.1, Occupational and Educational Personal Eye and Face Protection Devices
1926.102(a)(2)
NCDOL Photo Library
NCDOL Photo Library

## Slide 23: Eye and Face Protection
NCDOL Photo Library
NCDOL Photo Library
When employee vision requires the use of prescription lenses while needing eye protection, the employee shall either:
  Wear prescription safety glasses
  Wear protective safety goggles or Over the Glass (OTG) safety glasses over their normal prescription glasses, or
  Wear PPE that integrates prescription lenses into the design (such as with spectacle kits in full face respirators)
1926.102(a)(3)
NCDOL Photo Library
NCDOL Photo Library

## Slide 24: Eye and Face Protection
Protective safety eyewear shall:
  Provide adequate protection against specific hazards
  Be reasonably comfortable under working conditions
  Fit snugly and not interfere with movement
  Be durable
  Capable of being disinfected
  Easily cleanable
1926.102(a)(5)(i)-(vi)
NCDOL Photo Library
NCDOL Photo Library

## Slide 25: Foot Protection
Safety-toe footwear for employees shall meet requirements and specifications in ANSI Z41.1-1967, Men’s Safety-Toe Footwear
1926.96
NCDOL Photo Library
NCDOL Photo Library

## Slide 26: Respiratory Protection
Identical to 29 CFR 1910.134
  Written program
  Medical evaluation
  Fit testing
  Selection and use
  Maintenance and care
  Training
  Program evaluation
  Recordkeeping
1926.103
NCDOL Photo Library

## Slide 27: Safety Belts, Lifelines, Lanyards
Lifelines shall be secured above the point of operation to an anchorage or structural member
Minimum dead weight of 5,400 pounds
1926.104(b)
NCDOL Photo Library
NCDOL Photo Library

## Slide 28: Safety Belts, Lifelines, Lanyards
Safety belts and lanyard shall be a minimum of ½-inch nylon, or equivalent
  A fall no greater than 6 feet
Nominal breaking strength of 5,400 pounds
1926.104(d)
NCDOL Photo Library

## Slide 29: Safety Belts, Lifelines, Lanyards
All safety belts and lanyard hardware shall be drop forged or pressed steel, cadmium plated in accordance with Type 1, Class B plating specified in Federal Specification QQ-P-416
Surface shall be smooth and
free of sharp edges
1926.104(e)
NCDOL Photo Library
NCDOL Photo Library

## Slide 30: Safety Belts, Lifelines, Lanyards
All safety belts and lanyard hardware, except rivets, shall be capable of withstanding a tensile loading of 4,000 pounds without cracking, breaking, or taking a permanent deformation
1926.104(f)
NCDOL Photo Library
NCDOL Photo Library

## Slide 31: Safety Nets
Safety nets shall be provided when workplaces are more than 25 feet above ground, water surface, or other surfaces where use of ladders, scaffolds, catch platforms, temporary floors, safety lines, or safety belts are impractical
Where safety net protection
is required by this part,
operations shall not be
undertaken until net is in
place and has been tested
1926.105(a)-(b)
NCDOL Photo Library

## Slide 32: Safety Nets
Nets shall extend 8 feet beyond edge of the work surface where employees are exposed and shall be installed as close under the work surface as practical
1926.105(c)
NCDOL Photo Library
  It is intended that only one level of nets be required for bridge construction

## Slide 33: Working Over or Near Water
NCDOL Photo Library
Life jacket or buoyant work vests must be U.S. Coast Guard approved
1926.106(a)-(d)
  Prior to and after each use, buoyant work vests or life preservers shall be inspected for defects
  Ring buoys shall be provided for rescue operations
  Lifesaving skiff shall be
  immediately available

## Slide 34: Summary
General provisions of the standard
Basic hazard categories
Identification of hazard sources and personal protective equipment (PPE)
In this course, we covered the following:
NCDOL Photo Library

## Slide 35: Thank You For Attending!
Final Questions?
1-800-NC-LABOR
(1-800-625-2267)
www.labor.nc.gov