## Slide 1: Scaffolds
29 CFR 1926 – Subpart L
Presented by:
Notes: Revised 6/15/25
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
At the end of this course, students will be able to:
  Familiarize themselves with OSHA’s minimum requirements for scaffolds
  Recognize safe design, setup, and use of scaffolds
  Identify common scaffolding hazards
  Identify common abatement methods for scaffolding hazards

## Slide 3: Scaffolds
1926.450 - Scope, application and definitions applicable to this subpart
1926.451 - General requirements
1926.452 - Additional requirements applicable to specific types of scaffolds
1926.453 - Aerial lifts
1926.454 - Training requirements

## Slide 4: Scaffolds
Appendix A - Scaffold Specifications
Appendix B - (Reserved) Criteria for Determining the Feasibility of Providing Safe Access and Fall Protection for Scaffold Erectors and Dismantlers
Appendix C - List of National Consensus Standards
Appendix D - List of Training Topics for Scaffold Erectors and Dismantlers
Appendix E - Drawings and Illustrations
Note: These appendices are non-mandatory.
29 CFR 1926 Subpart L - Appendices

## Slide 5: Scope and Application
Covers all scaffolds used in workplaces
  Two categories for scaffolds
    Supported
    Suspended
Aerial lifts are covered in 1926.453
Does not apply to crane or derrick
suspended personnel platforms, which are covered by 1926.1431(a)-(e)
1926.450(a)

## Slide 6: General Requirements
Designed by qualified person
Constructed and loaded in accordance with that design
Appendix A (non-mandatory)
provides guidelines to assist in
complying with requirements
1926.451(a)(6)

## Slide 7: What makes this a good scaffold set up?

## Slide 8: What is wrong with this scaffold set up?

## Slide 9: General Requirements
Scaffold and scaffold components must support own weight and 4 times the maximum intended load.
  Includes personnel, equipment, and supply loads.
1926.451(a)(1)

## Slide 10: What are the hazards in this picture?

## Slide 11: Scaffold Platform Construction
Platforms on working levels of scaffolds must be fully planked or decked between front uprights and the guardrail supports.
1926.451(b)(1)

## Slide 12: Scaffold Platform Construction
No more than 1” space between adjacent units, and between platform and uprights.
Where necessary [e.g., to fit around uprights] maximum opening of 9½”.
1926.451(b)(1)(i)-(ii)

## Slide 13: Scaffold Platform Construction
Platforms used solely as walkways or performing scaffold erection or dismantling must be at least 18” wide.
1926.451(b)(2)

## Slide 14: Scaffold Platform Construction
The following scaffold platforms must be at least 12” wide:
  Ladder jack
  Top plate bracket
  Roof bracket
  Pump jack scaffold
1926.451(b)(2)(i)

## Slide 15: Scaffold Platform Construction
Front edge of all platforms:
  No more than 14” from the face of the work
Exception:
  Maximum distance – 3” for outrigger scaffolds
  Maximum distance – 18” for plastering and lathing operations
1926.451(b)(3)

## Slide 16: Scaffold Platform Construction
End of platform must extend over support at least 6”, unless cleated or restrained.
Platforms 10’ or shorter not to extend more than 12” over support.
Platforms more than 10’ not to extend more than 18” over support.
1926.451(b)(4), (b)(5)(i)-(ii)
Plank
cleated

## Slide 17: Scaffold Platform Construction
Each abutted end of scaffold planks must rest on a separate support surface.
1926.451(b)(6)

## Slide 18: Scaffold Platform Construction
When overlapping multiple platforms, overlap must occur only over supports and not less than 12” unless restrained to prevent movement.
1926.451(b)(7)

## Slide 19: Scaffold Platform Construction
Scaffold components must not be intermixed unless compatible and integrity maintained.
No modifications of mixed scaffold components unless approved by a competent person.
1926.451(b)(10)

## Slide 20: Criteria for Supported Scaffolds
Height to base width ratio of more than 4:1, must be restrained from tipping by:
  Guying
  Tying
  Bracing, or
  Equivalent
1926.451(c)(1)

## Slide 21: Criteria for Supported Scaffolds
1926.451(c)(1)(ii)
Guys, ties, and braces must be installed per manufacturer’s recommendations or at the closest horizontal member to the 4:1 height.
  Vertically every 20’ – 3’ or less in width
  Vertically every 26’ – more than 3’ wide
  Each end and horizontal intervals not to exceed 30’

## Slide 22: Criteria for Supported Scaffolds
1926.451(c)(2)
Poles, legs, posts, frames, and uprights must bear on base plates and mud sills or other adequate firm foundation.
Concrete slab is a firm
foundation and does
not require mud sills.

## Slide 23: Criteria for Supported Scaffolds
1926.451(c)(2)

## Slide 24: Criteria for Supported Scaffolds
1926.451(c)(2)(ii)
Unstable objects must not be used to support scaffolds or platform units.

## Slide 25: Criteria for Supported Scaffolds
1926.451(c)(2)(ii)

## Slide 26: Criteria for Supported Scaffolds
Unstable objects must not be used as working platforms.
1926.451(c)(2)(iii)

## Slide 27: Criteria for Supported Scaffolds
Front-end loaders and similar equipment must not be used to support scaffold platforms unless designed by manufacturer.
Forklifts used to support scaffold platform must have entire platform attached to forks.
Forklift not to be moved horizontally while platform is occupied.
1926.451(c)(2)(iv)-(v)

## Slide 28: Criteria for Supported Scaffolds
1926.451(c)(3)
Poles, legs, posts, frames, and uprights must be plumb and braced to prevent swaying and displacement.

## Slide 29: Criteria for Suspended Scaffolds
1926.451(d)

## Slide 30: Criteria for Suspended Scaffolds
1926.451(d)(1)
All suspension scaffold support devices such as outrigger beams, cornice hooks, parapet clamps, etc., shall rest on surfaces capable of supporting at least 4 times the imposed load from the scaffold.
Life Line

## Slide 31: Criteria for Suspended Scaffolds
1926.451(d)(3)(iii)-(v)
Only use counterweights specifically designed for the system in use.
Counterweights must be secured by mechanical means to outrigger beams to prevent accidental displacement.
Do not remove counterweights until final disassembly.

## Slide 32: Criteria for Suspended Scaffolds
1926.451(d)(3)(vii)-(x)
Tiebacks must be:
  Equivalent strength to suspension ropes
  Secured to structurally sound anchorage on building
  Installed perpendicular to face of building or structure

## Slide 33: Scaffold Access
Safe access must be provided to scaffold platforms.
  Portable ladders
  Hook-on ladders
  Stair towers
  Attachable ladders
  Stairway-type ladders
  Integral prefabricated scaffold access
1926.451(e)(1)-(6)

## Slide 34: Scaffold Access
Scaffold stairway/towers
  Stairrail – toprail and midrail
  Stairrails – 28”-37” from surface of tread
  Landing platform – at least 18” wide by 18” long at each level
  Stairway must be at least 18” wide
  Treads and landings – slip-resistant surfaces
1926.451(e)(4)

## Slide 35: Scaffold Access
Integral prefabricated scaffold access frames
  Designed and constructed for use as ladder rungs
  Rung length of at least 8”
  Uniformly spaced within each frame section
1926.451(e)(6)

## Slide 36
  Maximum spacing between rungs of 16 ¾”
  Have rest platforms at 35’ maximum vertical intervals on all supported scaffolds more than 35’ high
  Not to be used as a work platform if less than 11 ½”, unless using fall protection
1926.451(e)(6)
Scaffold Access

## Slide 37: Scaffold Access
Cross bracing on tubular welded frame scaffolds must not be used as means of access or egress.
1926.451(e)(9)(iv)

## Slide 38: Scaffold Use
Scaffold and scaffold components must not be overloaded.
Inspected for defects by competent person.
Immediately replaced,
repaired, or removed
from service if found
damaged.
1926.451(f)(1-4)

## Slide 39: Scaffold Use
Erected, moved, dismantled, or altered only under supervision of competent person
No work on snow, ice covered platforms
Tag lines on swinging loads
Protect suspension ropes from heat, acid, or
corrosive substances
No work during storms or high winds
No debris allowed to accumulate on platforms
1926.451(f)(7-13)

## Slide 40: Scaffold Use
Clearance between scaffolds and power lines:
  Insulated lines
    Less than 300 volts – 3’
    300 volts to 50 kV – 10’
    More than 50 kV – 10’ + 0.4” for each 1 kV over 50 kV
  Uninsulated lines
    Less than 50 kV – 10’
    More than 50 kV – 10’ + 0.4” for each 1 kV over 50 kV
1926.451(f)(6)

## Slide 41: Fall Protection
Fall protection (Personal Fall Arrest System (PFAS) or guardrails)
  1926.451(g)(1)(i-vi)
    PFAS and guardrails on suspension scaffolds
  1926.451(g)(2)
    PFAS required for erectors and dismantlers where feasible
  1926.451(g)(4)(ii)
    Toprails 38”- 45” high
  1926.451(g)(4)(iv)
    Midrails midway between toprail and platform surface
  1926.451(g)(4)(xv)
    Use cross-bracing in lieu of toprails or midrails in some cases
1926.451(g)

## Slide 42: Fall Protection
Employees on scaffold more than 10’ above a lower level must be protected from falling to that lower level.
1926.451(g)(1)

## Slide 43: Fall Protection
Employees on single-point or two-point adjustable suspension scaffold must be protected by both a personal fall arrest system and guardrail system.
1926.451(g)(1)(ii)

## Slide 44: Fall Protection
Employers must provide fall protection if feasible and does not create a greater hazard.
Competent person must determine:
  Feasibility and safety of providing fall protection during erecting and dismantling supported scaffold.
1926.451(g)(2)

## Slide 45: Fall Protection
1926.451(g)(4) - Guardrail systems that comply with Appendix A meet these requirements
1926.451(g)(4)(i) - Guardrail systems must be installed along all open sides and ends of platforms
1926.451(g)(4)(xiii) - Steel or plastic banding must not be used as a toprail or midrail
1926.451(g)(4)

## Slide 46: Fall Protection
Crossbracing may be used in place of the top or midrail when the crossing point of the braces is between:
  38”- 48” above work platform
  for toprail
  20”- 30” above work platform
  for midrail
1926.451(g)(4)(xv)

## Slide 47: Which is good? Which is bad and ugly?

## Slide 48: Falling Object Protection
Hardhats are required for employees on scaffolds.
1926.451(h)(1)

## Slide 49: Falling Object Protection
Erection of debris nets protect workers below from falling hand tools, debris, and other small objects.
1926.451(h)(1)

## Slide 50: Falling Object Protection
Area below the scaffold to which objects can fall must be barricaded.
Employees must not be permitted to enter the hazard area.
1926.451(h)(2)(i)

## Slide 51: Fall Protection
Where tools, material, or equipment is piled higher than top edge of toe board, paneling or screening extending from the toe board to the top of guardrail
must be installed.
1926.451(h)(2)(iii)

## Slide 52: Falling Object Protection
Toe board must be erected along edge of platform to prevent tools, materials, or equipment falling from scaffold.
  Minimum height – 3½”
  Securely fastened
1926.451(h)(4)(ii)

## Slide 53: Pole Scaffold
Pole scaffolds are an older type of supported scaffold in which every structural component, including uprights, braces and platforms are made of wood.
Runners extend over minimum of 2 poles.
Bearers extend minimum of 3” over outside edges of runners.
Bearers and runners not spliced between poles.
Since they are scratch built and seldom re-useable, they are rarely used today.
1926.452(a)(1)-(8)

## Slide 54: Pole Scaffold
Pole scaffolds over 60’ in height must be designed by registered professional engineer.
  Must be constructed and loaded in accordance with that design.
  Non-mandatory Appendix A can be used to comply with design and loading requirements for scaffolds under 60 feet in height.
1926.452(a)(10)

## Slide 55
Tube and coupler scaffolds over 125 feet in height must be designed by a registered professional engineer.
  Must be constructed and loaded in accordance with such design.
  Non-mandatory Appendix A can be used to comply with design and loading requirements for scaffolds under 125 feet in height.
Tube and Coupler Scaffolds
1926.452(b)(10)

## Slide 56
Scaffolds over 125 feet in height above base plates must be designed by a registered professional engineer.
Must be constructed and loaded in accordance with such design.
Fabricated Frame Scaffolds
1926.452(c)(6)

## Slide 57: Bricklayers Square Scaffold
These are scaffolds often made of wood used primarily for masonry.
Shall not exceed three tiers in height and shall be so constructed and arranged that one square rests directly above the other.
Upper tiers shall stand on a continuous row of planks laid across the next lower tier and shall be nailed down or otherwise secured to prevent displacement.
1926.452(e)

## Slide 58
Scaffolds must not be constructed or arranged more than two tiers or 10 feet, whichever is less.
Each horse must be placed directly over the horse in the tier below.
Horse Scaffold
1926.452(f)(1)-(2)

## Slide 59: Form Scaffolds
Each bracket, except those for wooden bracket-form scaffolds, must be attached to the supporting formwork or structure by one or more of the following:
  Nails
  A metal stud attachment device
  Welding
  Hooking over a secured structural supporting member
1926.452(g)(1)

## Slide 60: Roof Bracket Scaffold
Scaffold must be constructed to fit pitch of roof.
Must provide a level support for platform.
Platform must be at least 12” wide.
1926.452(h)(1)

## Slide 61: Outrigger Scaffold
Outrigger beams must be secured in place to prevent movement and securely braced at the fulcrum point to prevent tipping.
Entire supporting structure shall be securely braced to prevent any horizontal movement.
1926.452(i)(4)-(6)

## Slide 62: Pump Jack Scaffold
Poles must be secured to structure by rigid triangular bracing or equivalent – bottom, top, and other points as necessary.
Supported scaffold poles must bear on firm foundation.
1926.452(j)(2)

## Slide 63
Work benches must not be used as scaffold platforms.
  Is there safe access to this scaffold?
  Is there a fall protection violation?
1926.452(j)(4)
Pump Jack Scaffold

## Slide 64
Wood poles must be properly constructed.
  Are the poles properly secured?
  Is there a fall protection issue?
1926.452(j)(5)
Pump Jack Scaffold

## Slide 65
Are there pump jack scaffold violations here?

## Slide 66
Ladder Jack Scaffold
1926.452(k)
Bridged Platform
Over 20 feet ?
Platforms must not exceed a height of 20 feet.
Ladders must meet requirements of Subpart X – Stairways and Ladders.
Ladders must be placed, fastened, or equipped with devices to prevent slipping.
Platforms must not be bridged one to another.
Platform must be at least 12” wide.

## Slide 67: Mobile Scaffolds
Scaffolds must be properly braced.
Casters and wheel must be locked while in use.
Platforms must not extend out beyond base supports. – Unless outriggers are
used.
Caster stems and wheel stems must be pinned.
1926.452(w)

## Slide 68
Employees must not ride on scaffolds unless:
  Surface is within 3 degrees of level.
  Height to base ratio is 2:1 or less.
  Outrigger frames, when used, installed on both sides.
  Employees are not on any part of scaffold that extends beyond wheels or supports.
1926.452(w)
Mobile Scaffolds

## Slide 69
Power systems used to propel mobile
scaffolds must be designed for such
use.
Forklifts, trucks, and similar motor
vehicles must not be used to propel
scaffolds.
  Unless scaffold is designed for such
  propulsion systems.
1926.452(w)
Mobile Scaffolds

## Slide 70
Window jack scaffolds
Chicken ladders
Step, platform, and trestle ladder scaffolds
Needle beam
Float (ship)
Catenary scaffold
Interior hung scaffold
Multi-level scaffold
Two-point (swing stage)
Other Types of Scaffolds

## Slide 71: Aerial Lifts
Aerial lifts include the following:
  Extensible boom
  platforms
  Aerial ladders
  Articulating boom
  platforms
  Vertical towers
  Combination of any
  such device
1926.453(a)(1)

## Slide 72
Extensible and articulating boom platforms:
  Lift controls tested each day prior to use.
  Only authorized personnel must operate.
  Belting off to adjacent pole, structure, etc. not permitted.
  Employees must always stand firmly on floor of basket.
Aerial Lifts
1926.453(b)(2)

## Slide 73
  Brakes must be set.
  When outrigger used – positioned on pads or solid surface.
  Boom and basket load limits not exceeded.
  Aerial lift must not be moved while in working position.
  Exception – Equipment specially designed for operation.
Aerial Lifts
1926.453(b)(2)

## Slide 74
  Body belt must be worn, and lanyard attached to boom or basket.
    Body belts not acceptable as part of fall arrest system.
    Body belts are acceptable in a tethering or restraint system.
Aerial Lifts
1926.453(b)(2)

## Slide 75
Scissor lifts are not aerial lifts.
  Not covered under 1926.453
    Letter of interpretation – 8/1/00
  Scissor lifts meet the definition of a scaffold and must comply with requirements of a mobile scaffold.
Scissor Lifts are Not Aerial Lifts
1926.453

## Slide 76: Training Requirements
Trainer must be qualified in the subject matter.
Topics for employees who perform work on the scaffold:
  Nature of electrical, fall and falling object hazards
  Correct procedures for:
    Dealing with electrical hazards
    Erecting, maintaining, and disassembling fall protection systems
    Falling object protection systems being used
  Proper use of the scaffold and materials on scaffold
  Load capacities of scaffolds
  Requirements of this subpart
1926.454(a)

## Slide 77: Training Requirements
Employees that are involved in erecting, disassembling, moving, operating, repairing, maintaining, or inspecting a scaffold must be trained by a competent person.
Topics:
  Nature of scaffold hazards
  Correct procedures for erecting, disassembling, moving, operating, repairing, inspecting, and maintaining the type of scaffold in question
  Design criteria, maximum intended load-carrying capacity and intended use of the scaffold
  Other pertinent requirements of this subpart
1926.454(b)(2)

## Slide 78: Training Requirements
Retraining
  Employer has reason to believe that an employee lacks the skill or understanding needed for safe work involving the erection, use or dismantling of scaffolds.
  Where changes at the worksite present a new hazard.
  Where changes in the types of scaffolds, fall protection, falling object protection, or other equipment present a new hazard.
  Where inadequacies in an affected employee's work involving scaffolds indicate that the employee has not retained the requisite proficiency.
1926.454(c)

## Slide 79: Summary
In this course, we discussed the following:
  OSHA’s minimum requirements for scaffolds
  Safe design, setup, and use of scaffolds
  Hazard identification
  Abatement methods
Notes: 79

## Slide 80: Thank You For Attending!
Final Questions?