## Slide 1: Stairways and Ladders
1926 Subpart X
Notes: Revised 6/16/25
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
In this course, we will cover:
  Scope, application and definitions (1926.1050)
  General requirements (1926.1051)
  Stairways (1926.1052)
  Ladders (1926.1053)
  Training requirements (1926.1060)
  Appendix A, [Non-Mandatory] American National Standards Institute (ANSI) standards meeting requirements of 1926.1053(a)(1)
1926 Subpart X

## Slide 3: Scope and Application
Applies to all ladders and stairways used in:
  Construction
  Alteration repair
    Includes painting and decorating
  Demolition
1926.1050(a)

## Slide 4: General Requirements
A stairway or ladder must be provided for all personnel points of access where there is a break in elevation of 19 inches (48 cm) or more
1926.1051(a)
Is this a stairway or ladder?

## Slide 5: General Requirements
Use a double-cleated ladder (with center rail) or 2 or more ladders:
  When ladders are the only way to enter or exit a working area with 25 or more employees, or
  When a ladder will serve simultaneous two-way traffic
1926.1051(a)(2)
NCDOL Photo Library

## Slide 6: General Requirements
All points of access must be kept clear to permit free passage of employees
1926.1051(a)(3)
NCDOL Photo Library

## Slide 7: Temporary Stairways
1926.1052(a)(1)-(7)
NCDOL Photo Library

## Slide 8: Temporary Stairways
Except during construction, foot traffic is prohibited with:
  Pan stairs and skeleton metal stairs where permanent treads and landings are to be filled at a later date unless treads are filled and secured
1926.1052(b)(1)-(3)
Stair Pans –
Filled with Cement
NCDOL Photo Library

## Slide 9: Stairrails and Handrails
1926.1052(c)

## Slide 10: Stairrails and Handrails
Is this correct?
1926.1052(c)
NCDOL Photo Library

## Slide 11: Stairrails and Handrails
Stairways having four or more risers or rising more than 30 inches must be equipped with:
  At least one handrail, and
  One stairrail system along each
  unprotected side or edge
1926.1052(c)(1)(i)-(ii)

## Slide 12: Stairrails and Handrails
Stairrail and handrail systems must be:
  Capable of withstanding without failure 200 lbs.
  Surfaced to prevent injury to employees
  Constructed so not to constitute a projection
  hazard
1926.1052(c)(5), (8), (10)
The metal studs were used as the handrails and guardrails.
NCDOL Photo Library

## Slide 13: Handrails
Requirements are:
  Not more than 37″ and not less than 30″ from upper surface of rail to tread
  Provide adequate handhold for employees
  For a non-permanent part of structure: minimum 3″ between handrail and walls
1926.1052(c)(6), (9), (11)

## Slide 14: Stairrail Violation
1926.1052

## Slide 15: Stairrails and Handrails
Is this correct?
1926.1052(c)

## Slide 16: Stairrail System
Top edge of stairrail system:
  Must not be less than 36″ in height
  When serving as handrail, the height must not be
  more than 37″ and not less than 36″
  Midrail, screens, mesh,
  intermediate vertical members, or
  equivalent intermediate structural
  members, must be provided
  between top rail of system and
  stairway step
1926.1052(c)(3), (4), (7)

## Slide 17: Ladder Support
Self-supporting and non-self-supporting ladders must be capable of supporting at least four times the maximum intended load
  Except type 1A metal or plastic
  ladders must sustain at least
  3.3 times maximum intended load
1926.1053(a)(1)(i)-(ii)

## Slide 18: Ladder Support
Fixed ladders
  At least two loads of 250 pounds each, concentrated between any two consecutive attachments … plus anticipated loads caused by ice buildup, winds, rigging, and impact loads from ladder safety devices
1926.1053(a)(1)(iii)
NCDOL Photo Library

## Slide 19: Ladder Rungs
Ladder rungs, cleats, and steps must be parallel, level and uniformly spaced when the ladder is in position for use
Minimum distance between the side of individual rung/step must be
16 inches
1926.1053(a)(2)-(4)(i)

## Slide 20: Ladder Rungs
Rungs and steps of metal ladders must be corrugated, knurled, dimpled, coated with skid-resistant material or treated to minimize slipping
1926.1053(a)(6)(i)
NCDOL Photo Library

## Slide 21: Ladder Use
Ladders must not be tied or fastened together to extend unless by design
1926.1053(a)(7)
NCDOL Photo Library

## Slide 22: Ladder Use
A metal spreader or locking device must be provided on each stepladder to hold the front and back sections in an open position when the ladder is being used
1926.1053(a)(8)
Improper Use
Correct Setup
NCDOL Photo Library

## Slide 23: Ladder Use
Except when portable ladders are used to gain access to a fixed ladder, … when two or more separate ladders are used … the ladders must be offset by a platform or landing
1926.1053(a)(10)
NCDOL Photo Library

## Slide 24: Ladder Use
Wood ladders must not be coated with any opaque covering, except for identification or warning labels which may be placed on one face only of a siderail
1926.1053(a)(12)

## Slide 25: Ladder Use
When portable ladders are used for access to an upper landing surface, the ladder side rails must extend at least 3′ above the upper landing surface
1926.1053(b)(1)
Improper Use

## Slide 26: Ladder Use
Non-self-supporting ladders must be at an angle…. ¼ of working length from the foot to the top support – equates to a 4:1 ratio
1926.1053(b)(5)(i)

## Slide 27: Ladder Use
Ladders must be used only on stable and level surfaces unless secured to prevent accidental displacement
1926.1053(b)(6)
NCDOL Photo Library

## Slide 28: Ladder Use
Ladders must be used only for the purpose for which they were designed
1926.1053(b)(4)

## Slide 29: Ladder Use
Ladders must not be used on slippery surfaces unless secured or provided with slip-resistant feet to prevent accidental displacement
1926.1053(b)(7)-(8)
NCDOL Photo Library

## Slide 30: Ladder Use
Area around the top and bottom of ladders must be kept clear
1926.1053(b)(9)
NCDOL Photo Library

## Slide 31: Ladder Use
When ascending or descending a ladder, the user must face the ladder
Employee must use at least one hand to grasp the ladder when progressing up and/or down the ladder
1926.1053(b)(20)-(21)
NCDOL Photo Library
Improper Use

## Slide 32: Ladder Use
Is this correct?
NCDOL Photo Library
1926.1053(b)

## Slide 33: Ladder Use
Is this correct?

## Slide 34: Ladder Use
Is this correct?

## Slide 35: Ladder Use
Is this correct?
NCDOL Photo Library
1926.1053(b)

## Slide 36: Ladder Use
Is this correct?
NCDOL Photo Library
1926.1053(b)
NCDOL Photo Library

## Slide 37: Ladder Use
Non-self-supporting ladders must be at an angle … ¼ of working length from the foot to the top support – equates to a 4:1 ratio
1926.1053(b)(5)(i)
NCDOL Photo Library

## Slide 38: Ladder Use
Is this correct?
NCDOL Photo Library
NCDOL Photo Library

## Slide 39: Ladder Use
Ladders must be used only on stable and level surfaces unless secured to prevent accidental displacement
1926.1053(b)(6)
NCDOL Photo Library

## Slide 40: Ladder Use
Ladders must not be used on slippery surfaces unless secured or provided with slip-resistant feet to prevent accidental displacement
1926.1053(b)(7)
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library

## Slide 41: Ladder Use
Ladders placed in any location where they can be displaced by workplace activities or traffic, such as in passageways, doorways, or driveways must be secured to prevent accidental displacement, or a barricade must be used to keep the activities or traffic away from the ladder
1926.1053(b)(8)
NCDOL Photo Library
NCDOL Photo Library

## Slide 42: Ladder Use
Self-supporting top (top cap) or top step must not be used as a step
1926.1053(b)(13)
NCDOL Photo Library
NCDOL Photo Library

## Slide 43: Ladder Use
Can you identify the hazards?
NCDOL Photo Library
1926.1053(b)

## Slide 44: Ladder Use
Is this correct?
NCDOL Photo Library
1926.1053(b)

## Slide 45: Ladder Inspection
Ladders must be inspected by a competent person
Portable ladders with structural defects must be tagged and withdrawn from service until repaired
1926.1053(b)(15)-(16)
NCDOL Photo Library

## Slide 46: Ladder Safety
When ascending or descending a ladder, the user must face the ladder
Each employee must use at least one hand to grasp the ladder when progressing up and/or down the ladder
1926.1053(b)(20) – (21)
NCDOL Photo Library

## Slide 47: Training
Employer must provide a training program for each employee using ladders and stairways
  Competent person
    Nature of fall hazards in the work area
    Correct procedures for erecting, maintaining, and disassembling the fall protection systems to be used;
    Proper construction, use, placement, and care in handling of all stairways and ladders; and
    Maximum intended load-carrying capacities of ladders used
1926.1060

## Slide 48: 1926 Subpart X
American National Standard Institute for ladders:
  ANSI A14.1-1982 – Portable Wood
  ANSI A14.2-1982 – Portable Metal
  ANSI A14.3-1984 – Fixed
  ANSI A14.4-1979 – Job-Made Ladders
  ANSI A14.5-1982 – Portable Reinforced Plastic
Appendix A

## Slide 49: Summary
In this course we discussed the following:
  Scope, application and definitions (1926.1050)
  General requirements (1926.1051)
  Stairways (1926.1052)
  Ladders (1926.1053)
  Training requirements (1926.1060)
  Appendix A [Non-Mandatory]
1926 Subpart X

## Slide 50: Thank You For Attending!
Final Questions?