## Slide 1: Special Emphasis Program for Warehousing and Storage and Related Product Distribution Industries
OPN 145
Notes: Rev: 6/2025
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
At the end of this course, students will be aware of:
  Details of the Operational Procedure Notice (OPN) 145 – Special Emphasis Program (SEP) for Warehousing and Storage and Related Product Distribution Industries.
  Standards and hazards covered by
  this OPN.
  Employer and employee responsibilities
  related to the SEP.
OPN 145

## Slide 3: Purpose and Scope
This OPN describes the NC OSH Division’s SEP for inspections of grocery and related product wholesalers, warehousing and storage, distribution centers, delivery and courier services, and certain retail establishments where similar hazards may be found in their loading and storage areas.
OPN 145

## Slide 4: Special Emphasis Program Coverage
Covers North Carolina employers and sites in the following North American Industry Classification System (NAICS) codes:
  4244 - Grocery and Related Product Merchant Wholesalers
  493 - Warehousing and Storage
  492110 - Couriers and Express Delivery Services
  492210 - Local Messengers and Local Delivery

## Slide 5: Special Emphasis Program Coverage
It also includes NAICS codes for loading and storage areas of retail establishments that have the same or similar hazards as warehousing and distribution facilities:
  444110 - Home Centers
  444130 - Hardware Stores
  444190 - Other Building Material Dealers
  445110 - Supermarkets, and Other Grocery (except convenience stores
  452311 - Warehouse Clubs and Supercenters

## Slide 6: Strategic Management Plan
SEP goals for Federal Fiscal Year (FFY)
2024 - 2028 Strategic Management Plan:
  Reducing the rate of workplace injuries and illness by 2% by the end of FFY 2028.
  Reducing the NC Bureau of Labor Statistics (BLS) Days Away, Restricted or Transferred (DART) rate for establishments in North Carolina in this SEP by 1% per year.

## Slide 7: Strategic Management Plan Goals
Goals will be accomplished through:
  Identifying types and trends of injuries and illnesses.
  Providing hazard identification through inspections.
  Offering free, confidential consultative services.
  Forming alliances with those employers covered by this SEP.
  Developing training materials and publications.
  Providing free education and training.

## Slide 8: Recordkeeping Who Must Record?
All employers in North Carolina except:
  Any employer with 10 or fewer employees at all times for the previous calendar year unless OSHA or the BLS informs you in writing that you must keep records.
  Any employer who is on the updated list of NAICS codes.
Exemptions above do not change employers’ reporting requirements for fatalities, hospitalizations, loss of an eye or amputations.
1904.1 & 1904.2

## Slide 9: Recordkeeping What is Recordable?
Fatality, injury, or illness
  Work-related
  New case
  Meets one or more of the general recording criteria
1904.4(a)
NCDOL Photo Library

## Slide 10: Recordkeeping General Recording Criteria
Death
Days away from work
Restricted work or transfer to another job
Medical treatment beyond first aid
Loss of consciousness
Diagnosed as a significant injury or illness
1904.7(a)-(b)

## Slide 11: Recordkeeping OSHA Form 300 Log
29 CFR 1904
NCDOL Photo Library

## Slide 12: Recordkeeping Who Must Report?
All employers must still report:
  All work-related fatalities within 8 hours.
  All work-related in-patient hospitalizations of one or more employees within 24 hours.
  All work-related amputations within 24 hours.
  All work-related losses of an eye within 24 hours.
All employers must participate in OSHA and BLS surveys when requested.
1904, Subpart E

## Slide 13: Handling Materials General
Where mechanical equipment is used, sufficient safe clearances shall be maintained.
  Aisles
  Loading docks
  Through doorways
  Turns of passage
1910.176(a)
NCDOL Photo Library

## Slide 14: Handling Materials General
Aisles and passageways shall be kept clear and in good repair.
NCDOL Photo Library
1910.176(a)
Notes: 14

## Slide 15: Handling Materials General
Permanent aisles and passageways shall be marked.
NCDOL Photo Library
1910.176(a)

## Slide 16: Handling Materials Secure Storage
Storage of material shall not create a hazard.
1910.176(b)
NCDOL Photo Library
Notes: 16

## Slide 17: Walking-Working Surfaces General Requirements
Surface conditions
  All places of employment, passageways, storerooms, service rooms, and walking-working surfaces are kept in a clean, orderly, and sanitary condition.
    Free of hazards such as
    sharp or protruding objects,
    loose boards, corrosion,
    leaks, spills, snow and ice.
1910.22(a)(1)-(3)
NCDOL Photo Library
NC Photo Library

## Slide 18: Walking-Working Surfaces General Requirements
Is this in a clean, orderly, and sanitary condition?
1910.22(a)(1)-(3)
NCDOL Photo Library

## Slide 19: Walking-Working Surfaces Ladders
1910.23(a)
Employer must ensure that each ladder meets requirements of this section.
Covers all ladders, except when the ladder is:
  Used in emergency operations
  (firefighting, rescue, and tactical
  law enforcement operations) or
  training for these operations.
  Designed into or is an integral part
  of machines or equipment.

## Slide 20: Walking-Working Surfaces Ladders
Ladders are inspected before initial use in each work shift, and more frequently as necessary, to identify any visible defects that could cause employee injury.
1910.23(b)(9)
NCDOL Photo Library

## Slide 21: Walking-Working Surfaces Ladders
Any ladder with structural or other defects is immediately tagged “Dangerous: Do Not Use” or with similar language and removed from service until repaired or replaced.
1910.23(b)(10)

## Slide 22: Walking-Working Surfaces Stairways
General requirements
  Handrails, stairrail systems, and guardrail systems are provided as required by the standard.
  Vertical clearance above any stair tread to any overhead obstruction is at least 6 feet, 8 inches as measured from leading edge of tread (except for spiral stairs).
1910.25(b)
NCDOL Photo Library
> 6’8”

## Slide 23: Walking-Working Surfaces Stairways
Each flight of stairs having at least 3 treads and at least 4 risers is equipped with stairrail systems and handrails.
1910.28(b)(11)(ii)
NCDOL Photo Library

## Slide 24: Walking-Working Surfaces Handrails/Stair rail Systems
NCDOL Photo Library
Height criteria
  Handrails are not less than 30 inches and not more than 38 inches, as measured from leading edge of stair tread to top surface of handrail.
  Height of stairrail systems must meet not less than 42 inches from leading edge of stair tread to top surface of top rail.
1910.29(f)(1)
No Mid-rail
Stairrail
No Handrail

## Slide 25: Ergonomics
Ergonomics
  Greek derivation
    Ergo (work)
    Nomos (law)
  Interfacing man, machine and environment to optimize safety, productivity and comfort.
  “Fitting the task to the human”

## Slide 26: Ergonomics OSH Division Perspective
North Carolina employers can be cited for ergonomic violations without a specific OSHA standard for ergonomics.
Field Operations Manual (FOM) Chapter XVII – Ergonomic Inspection Procedures
  Phase 1
  Phase 2
  Phase 3
Citations for ergonomic violations are issued under the General Duty Clause (GDC).

## Slide 27: Ergonomics General Duty Clause
For GDC violations, the following criteria must be met:
  Employees must be exposed to a hazard.
  Hazard must be likely to cause death or serious physical harm.
  Hazard must be recognized in industry.
  Must be a feasible way to abate the hazard.
NCGS 95-129(1)

## Slide 28: Ergonomics Workplace Problems
Increased discomfort, pain, injury or illness
Workers’ compensation costs
Lost or restricted work time
Short- or long-term disability
Increased absenteeism
Greater turnover
Low morale
Decreased productivity and/or quality
NCDOL Photo Library

## Slide 29: Ergonomics Injuries
Definition
  Ergonomics is defined as the science related to man and his work, embodying the anatomic, physiologic, and mechanical principles affecting the efficient use of human energy.
Injury examples:
  Carpal tunnel syndrome; tendinitis; rotator cuff injuries (a shoulder problem); epicondylitis (an elbow problem); trigger finger; muscle strains and lower back injuries.
NCGS 95-129(1)

## Slide 30: Ergonomics Types of Back Injuries
Ligament sprains
Muscle or tendon strains
Lumbar strain/sprain
Low back pain
Disc disorders

## Slide 31: Musculoskeletal Disorders (MSD) Signs and Symptoms
Discomfort or pain
Numbness or tingling
Redness
Limited range of motion
Fullness, tightness or swelling
Weakness (trouble holding objects)
Early reporting of symptoms and early treatment may resolve problems without lost work time, restricted activity or surgery.
NCDOL Photo Library

## Slide 32: Ergonomics Proper Lifting Technique
Plan the lift and path.
Check the weight of the load.
Keep the load close to your body.
Face the load, do not twist.
Bend using your knees, not your back.
Lift with your legs, not your back.

## Slide 33: Exit Routes
1910.34(a)-(b)
Applies to all workplaces in general industry except mobile workplaces such as vehicles or vessels.
Exit routes are covered.
  Minimum requirements for exit routes to allow for the safe evacuation of employees during an emergency.
  Also covers the minimum requirements for emergency action plans (1910.38) and fire prevention plans (1910.39).

## Slide 34: Exit Routes Design Basic Requirements
Exit routes must be:
  Permanent
  Separated by fire resistant materials
  Openings into an exit must be limited
1910.36(a)(1)-(3)

## Slide 35: Exit Routes Number of Exit Routes
Number of exit routes must be adequate.
  Two exit routes
  More than two exit routes
  A single exit route
1910.36(b)

## Slide 36: Exit Routes Unlocked and Unrestricted
Must be able to open door from inside without keys, tools, or special knowledge.
  Panic bars that lock from the outside are permitted.
Must be free of device or alarm that could restrict emergency use if device or alarm fails.
May be locked from inside in mental, penal, or correctional facilities.
  And only if supervisory personnel are continuously on duty and there is an emergency plan.
1910.36(d)

## Slide 37: Exit Routes Maintenance and Safeguards
Danger to employees minimized.
Adequate and appropriate lighting and marking.
Fire retardant properties maintained.
Exit routes maintained during construction and repairs.
Employee alarm system must be operable.
1910.37(a)-(e)

## Slide 38: Exit Routes Danger to Employees Minimized
Kept free of explosive or highly flammable furnishings or other decorations.
Arranged so employees will not travel toward a high hazard area.
Must be free and unobstructed.
Safeguards designed to protect
employees during an emergency
must be in proper working order
at all times.
1910.37(a)

## Slide 39: Exit Routes Lighting and Marking
Adequately lighted.
Clearly visible and marked by a
sign reading “Exit”.
Free of decorations or signs that obscure visibility of exit.
If direction of travel to exit is not apparent, signs must be posted along exit access indicating direction of travel to nearest exit.
1910.37(b)(1)-(4)

## Slide 40: Fire Extinguishers General Requirements
Employer shall:
  Provide portable fire extinguishers.
  Mount, locate and identify them so they are readily accessible to employees without subjecting employees to possible injury.
1910.157(c)(1)

## Slide 41: Fire Extinguishers General Requirements
Only approved portable fire extinguishers shall be used.
1910.157(c)(2)

## Slide 42: Fire Extinguishers Selection and Distribution
Portable fire extinguishers shall be provided for employee use.
Selected and distributed based on the classes of anticipated workplace fires, size and degree of hazard.
1910.157(d)(1)

## Slide 43: Fire Extinguishers Selection and Distribution
Employer shall distribute:
  Class A fire extinguishers within a travel distance of 75 feet or less.
  Class A - Ordinary combustibles
    Wood
    Paper
    Plastic
    Cloth
    Rubber
1910.157(d)(2)

## Slide 44: Fire Extinguishers Inspection, Maintenance and Testing
Employer shall be responsible for the inspection, maintenance and testing of all portable fire extinguishers in the workplace.
Fire extinguishers or hose shall be visually inspected monthly.
1910.157(e)(1)-(2)

## Slide 45: Fire Extinguishers Inspection, Maintenance and Testing
Employer shall:
  Assure that fire extinguishers are subjected to an annual maintenance check.
  Record the annual maintenance date and retain record for one year.
  Record available to the Assistant
  Secretary upon request.
1910.157(e)(3)

## Slide 46: Heat Stress
Excessive heat in the work environment can lead to:
  Serious physical harm and/or death.
The keys are:
  Recognition of the hazards.
  Preventive measures.
NCDOL Photo Library
Notes: 46

## Slide 47: Heat Stress The “Perfect Storm”
Dark and heavy tight wool, nylon or polyester clothing
Working in direct sunlight
No water provided
Heavy physical work (such as using an axe or shovel)
High heat index (>115º F)
No breaks
No hat
Long workday
Worker not acclimated
NCDOL Photo Library
Notes: 47

## Slide 48: Heat Stress Causal Factors
Age, weight, degree of physical fitness
Degree of acclimatization, metabolism
Use of alcohol or drugs
A variety of medical conditions such as hypertension all affect a person’s sensitivity to heat
NCDOL Photo Library
Notes: 48

## Slide 49
Heat rash
Heat cramps
Heat exhaustion
Heat stroke
NCDOL Photo Library
Heat Stress Heat Disorders and Health Effects
Notes: 49

## Slide 50: Heat Stress Citations for Heat Stress?
Heat stress hazards are cited using the General Duty Clause.
  Each employer will furnish to each of his employees conditions of employment and a place of employment that are free from recognized hazards that are causing or are likely to cause death or serious physical harm to his employees.

## Slide 51: Heat Stress Action Items for Affected Employers
A heat illness prevention program
A heat acclimatization program
Access to an adequate supply of potable water
Means for employees to cool off (e.g., shaded areas, air-conditioned rooms, vehicles, fans)
Adequate number of rest periods
Appropriate protective clothing such as cooling vests
Heat stress training
First aid training (e.g., recognition, treatment of heat illnesses

## Slide 52
Covers safety requirements related to fire protection, design, maintenance, and use of:
  Forklifts
  Tractors
  Platform lift trucks
  Motorized hand trucks
  Other specialized industrial trucks
1910.178(a)(1)
Powered Industrial Trucks General Requirements
    Powered by electric motors or internal combustion engines

## Slide 53: Powered Industrial Trucks General Requirements
Powered Industrial Trucks “PITs” acquired and used by an employer shall meet the design requirements of:
  American National Standard for Powered Industrial Trucks, Part II, ANSI B56.1 – 1969’’, which is incorporated by reference as specified in § 1910.6.
Approved trucks shall bear a label or some other identifying mark indicating approval by the testing laboratory.
1910.178(a)(2)-(3)

## Slide 54
Modifications and additions which affect capacity and safe operation must have prior written approval from manufacturer.
Trucks equipped with front-end attachments, other than factory installed must:
  Be marked to identify the attachments.
  Show approximate weight of truck and attachment combination at maximum elevation with load laterally centered.
1910.178(a)(4-5)
Powered Industrial Trucks General Requirements

## Slide 55
All nameplates and markings in place and maintained in a legible condition.
The term, “approved truck or approved industrial truck”, means:
  A truck that is listed or approved for fire safety purposes for the intended use by a national recognized testing laboratory.
1910.178(a)(6)-(7)
Powered Industrial Trucks General Requirements

## Slide 56
NCDOL Photo Library
NCDOL Photo Library
Overhead guard used as protection against falling objects.
Load backrest extension used when necessary.
1910.178(m)(9)-(10)
Powered Industrial Trucks Truck Operations

## Slide 57
Employer shall ensure each powered industrial truck operator is competent to operate a powered industrial truck safely.
  As demonstrated by successful completion of training and evaluation.
1910.178(l)(1)(i)
NCDOL Photo Library
Powered Industrial Trucks Operator Training

## Slide 58
Brakes on trucks must be set and wheel chocks placed under rear wheels to prevent rolling.
Wheel stops or other positive protection provided to prevent railroad cars from moving.
Dockboards must be strong enough to carry imposed load.
Powered Industrial Trucks Trucks, Railroad Cars and Dockboards
1910.178(j)-(k)

## Slide 59: Machine Guarding Conveyors
Conveyors are safe when used correctly, but they can be dangerous, and even deadly, if workers fail to follow safety procedures when working on or around them.
  Use of guarding and not bypassed.
  Materials should be placed on the conveyor so that they will ride safely.
  Workers should remain alert and safeguard their hands; the moving material can create pinch points.
  How someone is dressed – loose clothing, long hair, and jewelry.
1910, Subpart O

## Slide 60: Machine Guarding Exposure of Blades
Exposure of blades
  Blades of fans less than
  7 feet above floor or working level must be
  guarded.
  Guard openings must
  be no larger than ½
  inch.
This fan does not comply
with the requirement.
1910.212(a)(5)

## Slide 61: Machine Guarding Fan Blades Not Properly Guarded
Corrective Action
  Install proper guard over fan blades with opening no larger than ½ inch.
These fans do not comply
with the requirement.

## Slide 62: Machine Guarding Mechanical Power-Transmission Apparatus 1910.219
Gears and belts must be guarded by complete enclosures or standard guard.
This does not comply with the requirement.

## Slide 63: Portable Powered Tools 1910.243(b)(2)
Pneumatic powered tools and hose
  Hose and hose connections shall be designed for pressure and service which they are subjected.
Proper Tool Connection
Improper Hose Connection

## Slide 64: Personal Protective Equipment
Worn to minimize exposure to hazards that cause serious workplace injuries and illnesses.
  PPE examples include hard hats, goggles, gloves and hearing protection.
  Should be a temporary measure.
NCDOL Photo Library

## Slide 65
Must be job and area based.
Requires written certification identifying the document as such including:
  Workplace evaluated
  Person certifying that the evaluation
  Date of hazard assessment
1910.132(d)
NCDOL Photo Library
Personal Protective Equipment
Hazard Assessment and Equipment Selection

## Slide 66
Training subjects:
  What PPE is required.
  When PPE is required.
  How to don, doff, adjust and wear PPE.
  Limitations of PPE.
  How to maintain and clean PPE.
  When to replace PPE.
1910.132(f)
Personal Protective Equipment
Training

## Slide 67: Occupational Noise Exposure
Noise - No employee shall be exposed above the permissible exposure limit (PEL).
  PEL = 90 decibels on the A scale (dBA) for an 8-hour time-weighted average (TWA).
Feasible administrative or
engineering controls are required.
Duration per day, hours | Sound level dBA slow response
8 | 90
6 | 92
4 | 95
3 | 97
2 | 100
1.5 | 102
1 | 105
0.5 | 110
0.25 or less | 115 NCDOL Photo Library
1910.95

## Slide 68: Medical Services and First Aid
Employer shall ensure the ready availability of medical personnel for advice and consultation on matters of plant health.
In the absence of an infirmary, clinic, or hospital in near proximity to the workplace which is used for the treatment of all injured employees, a person or persons shall be adequately trained to render first aid.
When required to have a person adequately trained to render first aid then adequate first aid supplies shall be readily available.
1910.151

## Slide 69: Medical Services and First Aid “In Near Proximity”
Letter of Interpretation (LOI)
  3/23/2007: Clarification of "in near proximity" and OSHA's discretion in enforcing first aid requirements in particular cases.
OSHA has long interpreted the term “in near proximity” to mean that emergency care must be available within no more than 3-4 minutes from the workplace.
OSHA can exercise discretion in some cases.
  Where the possibility of serious work-related injuries is less, such as an office.
    Up to 15 minutes may be reasonable.
1910.151

## Slide 70: Medical Services and First Aid Eye Wash Stations
Where the eyes or body of any person may be exposed to injurious corrosive materials, suitable facilities for quick drenching or flushing of the eyes and body shall be provided within the work area for immediate emergency use.
1910.151(c)

## Slide 71: Hazard Communication
Requires employers to provide information to their employees about the hazardous chemicals to which they are exposed by the following means:
  Hazard communication program
  Labels and other forms of warning
  Safety data sheets (SDS)
  Information and training
1910.1200(b)(1)

## Slide 72: Hazard Communication
1910.1200(b)(2)
Nova Development
Applies to chemicals known to be present in the workplace.
Employees that may have a potential for exposure:
  Under normal conditions, or
  Foreseeable emergency.
NCDOL Photo Library

## Slide 73: Hazard Communication Key Elements
Hazard classification
Written program
Labeling
Safety Data Sheets
Employee training
1910.1200

## Slide 74: Process Safety Management
Prevent catastrophic releases of highly hazardous chemicals.
Grocery warehouse operations often require large scale industrial refrigeration. The quantities of ammonia required for these operations often place these operations within the Process Safety Management (PSM) Threshold Quantities.
1910.119

## Slide 75: Process Safety Management Threshold Quantity (TQ)
Toxic or reactive process chemical(s) ≥ TQ:
  Chemicals covered in appendix A
  Ammonia TQ = 10,000 Lbs.
  Chlorine TQ = 1,500 Lbs.
  Flammable liquids and gasses TQ =10,000 Lbs.
    (Except [A] and [B])
1910.119(a)

## Slide 76: Summary
Students should now be aware of:
  Details of OPN 145 - Special Emphasis Program for Warehousing and Storage and Related Production Distribution Industries.
  Standards and hazards covered by this OPN.
  Employer and employee responsibilities related to the SEP.

## Slide 77: Thank You For Attending!
Final Questions?