## Slide 1: Struck By/Caught Between
Notes: Revised 6/16/25
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
After this course, students will be able to:
  Recognize potential struck-by/caught-in or between situations
  Identify struck-by/caught-in or between hazards
  Evaluate control measures for struck-by/caught-in or between hazards
NCDOL Photo Library

## Slide 3
Goal to reduce occupational exposures to amputations
Struck by and caught between injuries
  Lockout/tagout
  Machine guarding
Increase outreach to employers and employees
  Training events (Internal and external)
  Compliance inspections
  Consultation visits
  Publications
Amputations must be reported within 24 hours
Amputations Special Emphasis Program

## Slide 4: Definitions
Competent person
  “One who is capable of identifying existing and predictable hazards in the surroundings or working conditions which are unsanitary, hazardous, or dangerous to employees, and who has authorization to take prompt corrective measures to eliminate them.”
1926.32(f)

## Slide 5: Struck-By Hazards
Struck-by injuries are produced by forcible contact or impact between the injured person and an object or piece of equipment.
Struck-by hazards are categorized as follows:
  Struck-by flying object
  Struck-by falling object
  Struck-by swinging object
  Struck-by rolling object

## Slide 6: Struck-By Hazards
Struck-by examples:
  Tractor trailer, truck or vehicle
  A counterweight from piece of equipment
  Falling tree, tree-top or limbs/branches
  Precast walls
  Building materials
  Motor graders
  Fly wheels
  Man-lifts
  Forklifts
NCDOL Photo Library

## Slide 7: Caught-In or Between Hazards
Hazards causing a person to be squeezed, caught, crushed, pinched, or compressed between two or more objects, or between parts of an object.

## Slide 8: Caught-In or Between Hazards
Caught-in or between examples:
  Between a wall and tractor trailer
  Caught in/between truck tire and pavement
  Caught in/between dock leveler
  Caught in woodchipper
NCDOL Photo Library

## Slide 9: Struck By/Caught Between Causes
Most of these are a direct result of:
  Materials handling, storage, use, and disposal
  Construction equipment
  Motor vehicles
  Tools and equipment
  Falling trees
  Woodchipper

## Slide 10: Construction Equipment
Examples of hazards with construction equipment:
  Worker crushed by a compactor/roller
    Highway construction area/site, when it backed over him
  Operator of a backhoe installing sewer lines
    Bucket struck an adjacent tree which was rotten, causing the tree to fall, striking another worker in the head that was standing in a 2-foot-deep trench

## Slide 11: Construction Equipment
No visibility zone:
  Backhoe loader
    Educate workers how to
    approach all construction
    equipment while in operation.

## Slide 12: Construction Equipment
Safety issues:
  Overhead hazards
  Low visibility

## Slide 13: Construction Equipment
Safe work practices:
  Roll-over protection structures - “ROPS”
  Seatbelts

## Slide 14: Construction Equipment
Rollover protective structures:
  Employers are responsible for requiring the wearing of appropriate personal protective equipment.
    Failure to use “seat belts” is citable under 1926.28(a).
1926.602(a)(2)

## Slide 15: Construction Equipment
No visibility zone:
  Do not drive a vehicle in reverse gear with an obstructed rear view, unless it has an audible reverse alarm, or another worker signals that it is safe.

## Slide 16: Construction Equipment
No visibility zone:
  Do not drive equipment in reverse gear with an obstructed rear view, unless it has an audible reverse alarm, or another worker signals that it is safe.

## Slide 17: Construction Equipment
Hazard issues:
  Workers struck and run over by moving vehicles and equipment.
  Workers struck by automobiles while in work zones.
  Vehicles/equipment operated in reverse gear with obstructed rear view.
    Remember, spotters themselves can be at risk for injury or even death.
NCDOL Photo Library
NCDOL Photo Library

## Slide 18: Motor Vehicles
Safe work practices:
  When vehicle safety practices are not observed, there is a risk of being struck by oncoming vehicles.
    Garbage truck is driving down the wrong side of the street.

## Slide 19: Motor Vehicles
Hazard issues:
  Use traffic signs, barricades or flaggers when construction takes place near public roadways.
    Workers must be highly visible at all times, day or night.
    Safety apparel, such as red or orange vests, are required.
      If worn for night work,
      must be of reflective
      material.
Employee

## Slide 20: Motor Vehicles
Safe work practices:
  When vehicle safety practices are not observed, there is a risk of being struck by vehicles.
NCDOL Photo Library

## Slide 21: Motor Vehicles
Safe work practices:
  Provide an area of separation between traffic flow and work area.

## Slide 22: Motor Vehicles
Safe work practices:
  Equipment being operated near traffic must be protected by adequate buffer space.
NCDOL Photo Library
NCDOL Photo Library

## Slide 23: Motor Vehicles
Personal protective equipment:
  All workers exposed to the risks of moving roadway traffic or construction equipment should wear high-visibility safety apparel.
NCDOL Photo Library

## Slide 24: Motor Vehicles
What are the safety issues?

## Slide 25: Materials Handling and Storage
Examples:
  Worker was standing on the main floor of a one-story single-family residence.
    Several trusses collapsed falling onto the worker.
  Worker was trying to move a vertically stacked pile of 16 pieces of 12' by 4' drywall.
    Drywall shifted pinning him between the stack of drywall and the door jam.

## Slide 26: Materials Handling and Storage
Safety issues:
  Improperly stored materials
  Incorrectly cutting ties or other securing devices
  Improper loading and unloading

## Slide 27: Materials Handling and Storage
Safety issues:
  Improperly stored materials
  Incorrectly cutting ties or other securing devices
  Improper loading and unloading

## Slide 28: Materials Handling and Storage
What safety issues do you see?
  Electrical safety
  Falling object protection

## Slide 29: Materials Handling and Storage
What are the safety issues?
  Housekeeping

## Slide 30: Materials Handling and Storage
Rigging safety issues:
  Using defective rigging equipment
  Excessive loading

## Slide 31: Materials Handling and Storage
What are the rigging safety issues?
  Qualified rigger

## Slide 32: Materials Handling and Storage
Rigging safe work practices:
  Load should not exceed rated capacity
  Protect sling from sharp corners
  Know center of gravity of load

## Slide 33: Materials Handling and Storage
Rigging safe work practices:
  Inspect the rigging
  Keep personnel clear
  Never leave load unattended
  Wear hardhats when lifting

## Slide 34: Tools and Equipment
Safety issues:
  Improper work procedures
    Machine guards
  Use of defective equipment

## Slide 35: Tools and Equipment
Are there safety issues?
  Jacks must have a rated capacity
    1926.303(a)(1) and 1926.305(d)(1)(i)

## Slide 36: Tools and Equipment
Are there safety issues?
1926.303(c)(6)

## Slide 37: Tools and Equipment
What are the safety issues?

## Slide 38: Falling Trees
What are the hazards?
  Trees
  Falling branches

## Slide 39: Woodchippers
What are the hazards?
NCDOL Photo Library

## Slide 40: Preventing Struck By/Caught Between Injuries
Comprehensive Safety Program
  Development, implementation, and enforcement of program for workers
    Includes training in the recognition and avoidance of unsafe work conditions and instruction in safe work practices
    If a multilingual workforce, instruction should be in the language understood by the worker
    Ensures appropriate PPE and usage

## Slide 41: Summary
In this course, we covered:
  Recognizing potential struck-by/caught-in or between situations
  Identifying struck-by/caught-in or between hazards
  Evaluating control measures for struck-by/caught-in or between hazards
NCDOL Photo Library

## Slide 42: Thank You For Attending!
Final Questions?